## Slide 1: WF on enhanced SU-MIMO
Huawei, HiSilicon, LGE, Intel
3GPP TSG-RAN WG4 Meeting #82 Athens, Greece, 13 - 17 February, 2017
Agenda Item: 7.19.4
R4-1702459

## Slide 2: Background
In RAN4#81, companies are encouraged to provide inputs on the scenarios and reference receivers analysis in RAN4 #82.
  Based on collecting simulation results in RAN4#82, RAN4 will identify target scenarios for performance requirements definition
To Specify final test cases for UE demodulation performance requirements, confirmation for some test cases and identify some scenarios for further investigation are needed.
Companies are encouraged to provide further inputs on the controversial scenarios in RAN4 #82bis.

## Slide 3: Scenarios for confirmation
MIMO Rank 2 scenarios
  TM4 2x4 + 16QAM 1/2, ULA medium
  TM9 2x4 + 16QAM 1/2, ULA medium
MIMO Rank 3 scenarios
  TM3 4x4 + 16QAM, ULA medium A
Define requirements for above scenarios
Companies are encouraged to further check the results for better alignment

## Slide 4: Scenarios for further evaluations
MIMO Rank 2 scenario
  TM4/9 4x4 + 256QAM, ULA low/medium A
  TM4/9 4x4 + 64QAM, ULA medium/medium A
MIMO Rank 4 scenarios
  TM4/9 4x4 + 16QAM, XPOL medium A
Companies are encouraged to provide results for above scenarios in next meeting

## Slide 5: Scenarios with interference
Do not introduce interference scenario in Rel-14 enhanced SU-MIMO
Keep Rel-12 SU-MIMO interference scenario

## Slide 6: Feature/Capability signaling
Enhanced SU-MIMO IM feature
  Optional feature for 4 RX capable UEs
  Option 1 : Single feature for rank 2,3,4 SU-MIMO IM
  Option 2 : Two features
    4RX SU-MIMO for rank 2
    4RX SU-MIMO for rank 3,4
  Support of 2RX R-ML does not imply the support of 4RX R-ML
  FFS if support of 4RX R-ML implies the support of 2RX R-ML
Enhanced SU-MIMO IM Capability signaling
  No UE capability signaling

## Slide 7: CSI tests
Companies are encouraged to provide analyses on CSI tests in next meeting