## Slide 1: MIMO OTA Way Forward
Intel Corporation, SGS Wireless
3GPP TSG-RAN WG4 Meeting #82bis
Spokane, US, April 3 – 7, 2017
Agenda: 7.11.1
R4-1702934

## Slide 2: Performance (1)
Impact of emerging UE behavior on TRMS
  The possible activation of a gain stage has been observed in the testing [R4-1703744]
  A correction of the MPAC measurement procedure is needed to quantify such UE performance at the lowest possible downlink power level – i.e. with the gain stage(s) enabled
  A correction of the definition of the sensitivity value per azimuth position (the P_MODE) is needed
  CRs to update the procedures in TR37.977 and P_MODE definition in TS37.144 are requested by the next meeting
  An email discussion on the MIMO OTA reflector following RAN4#82bis is suggested to resolve this issue
    Discussion start: April 10, 2017
    Discussion close: April 14, 2017

## Slide 3: Performance (2)
Lab alignment
  Measurements have concluded at both labs participating in the alignment activity; efforts to analyze and compare the data are ongoing
  Limits for the power validation procedure
    Total (V+H) power target = -80 dBm/15 kHz [R4-1609157]
      A CR to capture the total power target in TR37.977 is needed for the next meeting
    Measurement procedure and the maximum deviation in measured V power across labs using the same calibration reference dipole are TBD
      Proposals on the measurement procedure and deviation value are requested for the next meeting
      A CR to capture the power validation procedure and acceptance criterion in TR37.977 is needed for the next meeting
Data for performance requirement definition
  Labs which have demonstrated alignment are encouraged to contribute measured device data and proposals for the TRMS requirement definition

## Slide 4: Harmonization (1)
Impact of emerging UE behavior on harmonization
  The possible activation of a gain stage has been observed in the testing [R4-1703744]
  Corrections of the RC+CE and RTS measurement procedures are needed to quantify such UE performance at the lowest possible downlink power level – i.e. with the gain stage(s) enabled
  A correction of the definition of the sensitivity value per stirring state is needed for the RC+CE results
  The definition of the sensitivity value per azimuth position for RTS is reused from the corrected P_MODE definition

## Slide 5: Harmonization (2)
Upon completion of the lab alignment activity, it is requested to make the reference DUTs and calibration dipoles available to CATR so that the alignment of the CATR MPAC chamber can be verified

## Slide 6: Harmonization (3)
RTS work plan
  Definition of isolation for the 2nd stage
    CR proposed with 15 dB limit and [50] RSAP average
    [50] RSAP averages will be confirmed with measurements at next meeting
  Channel model validation for RTS
    The procedures used for channel model validation of RTS need to be defined in the TR at next meeting
    The CR with proposed limits will be presented at the next meeting focussing on the correlation-based implementation
  Applicability of UE capabilities to RTS test method needs to be defined and impact on harmonization testing needs to be considered