## Slide 1: WF for 4Rx CA 256QAM(1/2 layer) and 3/4 layers tests in Rel-14
Ericsson, AT&T, China Telecom, CMCC, NTT Docomo, SoftBank
3GPP TSG-RAN WG4 Meeting #82bis R4-1703419 Spokane, USA, 3rd-7th April, 2017
Agenda Item: 7.21.2.2
Document Type: Approval

## Slide 2: Background
256QAM(1/2 layers) tests are important deployment scenarios under CA to reach higher TP
Higher layers (3/4 layers) tests are also important deployment scenarios under CA to reach higher TP
Different CC has different propagation channel which may require different UE implementation properly to ensure both 256QAM(1/2 layers) and higher layers (3/4 layers) tests under CA deployment.

## Slide 3: Way forward
RAN4 agrees to specify the following performance test cases for Rel-14 4Rx CA WI
  256QAM(1/2 layers) tests
    The tests will be specified with single carrier requirement for both 2 Rx and 4Rx on multiple bandwidths on 5, 10, 15, 20MHz.
  Higher layers (3/4 layers) tests
    The tests will be specified with single carrier requirement for 4Rx on multiple bandwidths on 5, 10, 15, 20MHz.
The above tests will be specified with at least 2 CCs.
The other test scenarios are TBD.