## Slide 1: Further study on spreading method
Agenda item: 10.3.3
Document for: Approval
Source: Orange
R4-1703832
3GPP TSG-RAN WG4 Meeting #82bis
Spoken, USA, 3 - 7 April, 2017

## Slide 2: Background
Spreading method with sequence [1,-1] can be applied on the edge PRBs for different purposes
It can be applied on both F-OFDM and WOLA [1]
When it applies on F-OFDM, the edge EVM issue inherited in F-OFDM can be resolved by de-spreading [1]
When it applies on WOLA, spectral efficiency can be increased due to the additional modulated PRBs  higher spectrum utilization [1]
[1] R4-1701760: On spectral utilization and EVM for NR, Orange

## Slide 3: Further discussions on
Spectrum utilization gain
BLER evaluation
Complexity evaluation
PAPR evaluation
EVM enhancement for F-OFDM

## Slide 4: Spectrum utilization gain
Assume that
  spreading method is applied on WOLA
  fixed window length: 2% of symbol length (SRRC window)
  10 MHz bandwidth
  baseline is LTE spectral utilization 90%
For WOLA without spreading method, we consider two allocation cases:1 additional PRB is allocated on one side (case 1), 1 additional PRB is allocated in the center carrier frequency (case 2).
1
2
25
49
26
1
2
50
51
DC
CASE 1
1
2
25
49
26
1
2
50
DC
CASE 2
PRB index
PRB index
51

## Slide 5: Spectral efficiency gain (2)
The spreading method is applied at edge PRBs with sequence [1,-1]
Since the spreading reduces the spectral efficiency, the effective spectrum utilization gain is 1 PRB compared to WOLA with 51 PRBs
PRB index
a
-a
b
-b
c
-c
subcarrier index in 1 PRB of edge PRB
f
-f
1
2
3
4
5
6
11
12
spreading
method
a, b, c, …, f, are complex symbols
1
2
25
49
26
1
2
50
51
DC
52
53
54

## Slide 6: Power spectral density comparison
WOLA case 1 cannot fit into the spectrum mask, while WOLA case 2 can fit into the mask, implying the max SU for WOLA with 2% window length

## Slide 7: Observation 1:
Spreading method can help WOLA to increase the spectral efficiency. The effective spectral efficiency gain is 1 PRB for 10 MHz bandwidth and 15 kHz SCS

## Slide 8: BLER improvement due to processing gain
The de-spreading on Rx provides processing gain which enhances the protection from the interference for the edge PRBs (spreading applied PRBs)

## Slide 9: BLER improvement due to processing gain
The de-spreading on Rx provides processing gain which enhances the robustness against the interference for the edge PRBs (spreading applied PRBs)

## Slide 10: Observation 2:
Besides the spectrum utilization gain, the spreading method can also enhance the robustness on the spreading applied edge PRBs

## Slide 11: Complexity
The spreading sequence is [1,-1], thus on Tx side, no computational complexity is added
On Rx side, the de-spreading involves a summation of two consecutive subcarriers and a division by 2. Thus, in practice, only additional complex additions are consumed at Rx
In our example of 10 MHz bandwidth, the additional computational complexity, corresponding to the de-spreading process on 4 edge PRBs, is < 0.2% complex additions and no additional multiplication (only compare with FFT demodulation)
Observation: the complexity increase due to spreading/de-spreading is completely negligible

## Slide 12: Observation 3:
The complexity increase due to spreading/de-spreading is negligible

## Slide 13: PAPR evaluation
Spreading method is only applied on the edge PRBs, leading to no impact on the PAPR

## Slide 14: Observation 4:
Applying spreading on the edge PRBs, will not impact the overall signal PAPR.

## Slide 15: EVM improvement for f-OFDM using spreading method on additional edge PRBs
Edge EVM can be improved and no remarkable impact on SU

## Slide 16: Observation 5:
Applying the spreading method on the edge PRBs for F-OFDM can resolve the edge EVM issue. As a result, all PRBs can be allocated with high order constellations.

## Slide 17: Conclusions
The spreading method can help WOLA to increase the spectral efficiency. The effective spectral efficiency gain is 1 PRB for 10 MHz bandwidth and 15 kHz SCS
The spreading method can enhance the robustness on the spreading applied edge PRBs
The complexity increase due to spreading/de-spreading is negligible
Applying spreading on the edge PRBs, will not impact the overall signal PAPR.
The spreading method can help F-OFDM to remove the EVM issue
Proposal
  Special PRB with spreading method, which is configurable for network, should be supported by NR and be taken into account for the specification of minimum level of spectrum utilization.

## Slide 18: Thanks