## Slide 1: WF on MUST performance tests
MediaTek
3GPP TSG-RAN WG4 Meeting #82b Spokane, WA, USA, 3rd - 7th April 2017
Agenda Item: 7.24.1
R4-1704153

## Slide 2: Background
Agreement during online discussion
  MUST Case 1 and 2
    One test case for TM2, Near UE Rank 1, Far UE Rank 1
    One test case in TM3.
    One test case for testing the power allocation behaviour when p-a-must is configured.
      The value of p-a-must can be 3 dB lower than p-a.
    Fixed Near/Far UE power ratios
  MUST Case 3
    R-ML receiver as a baseline for MuST Case 3
    One interference layer for all test cases

## Slide 3: Way Forward
MUST Case 1 and Case 2
  Agreed test cases: A1 and A2
  A3 is to be confirmed in the next meeting
  Other detail test configurations to be discussed in Email reflector before April 21
  Companies are encouraged to provide alignment results and impairment results in the next meeting
Test | TM | Rank (N+F) | p-a (dB) | p-a-must (dB) | Power ratio | MCS | Antenna | Channel
A1 | 2 | 1+1 | -3 | N/A | 264.5/289 (3rd) | #9 | 2x2 low | EVA5
A2 | 3 | 2+2 | 0 | -3 | 144.5/167 (2nd) | #10 |  | 
A3 | 4 | 2+1 | 0 | -3 | 128/138 (2rd) | #10 |  | 

## Slide 4: Way Forward
MUST Case 3
  Agreed test cases
    Applicability rule:
      UE supporting only Rel-10 DMRS and k-max up to 1 is tested by B1
      UE supporting Rel-13 DMRS and k-max up to 1 is tested by B2
      UE supporting Rel-13 DMRS and k-max up to 3 is tested by B3
      Same requirement to be shared by B1, B2 and B3
    Precoder assumption
      Random: same rule as 8.3.1.1 Test#2
      Constrained: Rank-2 precoder, as mentioned in R4-1703247
  Other detail test configurations to be discussed in Email reflector before April 21
  Companies are encouraged to provide alignment results and impairment results in the next meeting
Test | OCC length | k-max | BMUST | Antenna (FDD and TDD) | Channel | Target-UE MCS | Interf.-UE MOD | Precoder assumption
B1 | 2 | 1 | 2 | 4X2 low | EPA5 | #16 | [QPSK, 16QAM] | [Random, constrained]
B2 | 4 | 1 | 4 |  |  |  |  | 
B3 | 4 | 3 | 6 |  |  |  |  | 

## Slide 5: For information
Simulation assumptions for MUST Case 1 and Case 2
Parameter | Unit | Value (FDD) | Value (TDD)
Bandwidth | MHz | 10 | 
Duplex mode |  | FDD | TDD
Uplink downlink configuration |  | N/A | 1
Special subframe configuration |  | N/A | 4
Cyclic Prefix |  | Normal | 
Cell_ID |  | 0 | 
 | dB | A1: -3 A2: 0 | 
 | dB | A1: -3 A2: 0 | 
 | dB | 0 | 
Cell-specific reference signals |  | Antenna ports 0,1 | 
Propagation Condition |  | EVA5 | 
Correlation Matrix and Antenna Configuration |  | 2x2 Low | 
Subframe # with PDSCH |  | #0, 1, 2, 3, 4, 6, 7, 8, 9 | #0, 1, 4, 6, 9
Number of HARQ processes per component carrier | Processes | 8 | 7
Maximum number of HARQ transmission |  | 4 | 
Redundancy version coding sequence |  | {0,1,2,3} for QPSK and 16QAM | 
Number of OFDM symbols for PDCCH | OFDM symbols | 2 | 

## Slide 6: For information
Simulation assumptions for MUST Case 3
Parameter | Unit | Value (FDD) | Value (TDD)
Bandwidth | MHz | 10 | 
Duplex mode |  | FDD | TDD
Uplink downlink configuration |  | N/A | 1
Special subframe configuration |  | N/A | 4
Cyclic Prefix |  | Normal | 
Cell_ID |  | 0 | 
 | dB | 0 | 
 | dB | 0 | 
 | dB | -3 | 
Cell-specific reference signals |  | Antenna ports 0,1 | 
CSI-RS periodicity and subframe offset TCSI-RS / ∆CSI-RS | Subframes | 5 / 2 | 5/4
CSI reference signal configuration |  | 3 | 3
Zero-power CSI-RS configuration ICSI-RS / ZeroPowerCSI-RS bitmap | Subframes / bitmap | 3 / 0001000000000000 | 4 / 0010000000000000
Propagation Condition |  | EPA5 | 
Correlation Matrix and Antenna Configuration |  | 4x2 Low | 
Subframe # with PDSCH |  | #0, 1, 2, 3, 4, 6, 7, 8, 9 | #0, 1, 4, 6, 9
Maximum number of HARQ transmission |  | 4 | 
Redundancy version coding sequence |  | {0,1,2,3} for QPSK and 16QAM | 
Number of OFDM symbols for PDCCH | OFDM symbols | 2 |