## Slide 1: Way Forward on PRACH Repetition Level Selection in feMTC
Ericsson, [Nokia, Huawei, Qualcom, Intel, ...]
R4-1704258
3GPP RAN WG4 Radio #82bis
Spokane, WA, US, April 3 – 7, 2017

## Slide 2: Justification
Erroneous selection of PRACH repetition level has a negative impact on UE battery consumption and on system performance
When 2 TX ports are used by the BS, the UE can benefit from diversity provided by two radio paths when deciding on PRACH repetition level
CRS from TX ports 0 and 1 are comprised in the same OFDM symbol and thus are acquired in the same FFT operation

## Slide 3: Background
At reselection and handover the UE acquires information on number of TX ports from system information
Before acquiring system information the UE does not know whether TX port 0 or TX ports 0 and 1 are present
Blind detection on number of TX ports is error-prone particularly at SINR levels where PRACH repetition is needed – thus it shall be avoided
Additional measurement time between system information acquisition and random access is undesirable

## Slide 4: Proposed solution to be studied
The UE maintains two L1 filtering processes for tentative target cells for which number of TX ports is unknown
  Filter process 0, e.g. TX port 0 only
  Filter process 1, e.g. combined TX port 0 and 1
Mobility is based on TX port 0 only unless UE has information on number of TX ports
PRACH repetition selection is based on Filter process 0 in case system information indicates presence of TX port 0 only, and Filter process 1 in case the same information indicates presence of TX ports 0 and 1.

## Slide 5: Feasibility study for RAN4#83
Companies are encouraged to study the complexity increase and the reduction in power consumption resulting from the proposed solution to more accurate repetition level selection
Companies are encouraged to study combination schemes for measurements from TX ports 0 and 1 (RAN1 specifications are non-limiting in this respect)