## Slide 1: WF for test scenario for performance requirement for FeMBMS
Ericsson, Qualcomm
3GPP TSG-RAN WG4 Meeting #82bis R4-1704281 Spokane, USA, 3rd-7th April, 2017
Document Type: Approval

## Slide 2: Channel model
It’s proposed for subcarrier spacing 15kHz and 7.5kHz tests the existing MBMS channel model could be reused. For subcarrier spacing 1.25kHz it’s proposed to define a new channel model as following.
Maximum Doppler frequency [5Hz] |  | 
Relative Delay [ns] |  | Relative Mean Power [dB] (1.25k/7.5k/15kHz numerology)
Extended Delay Spread [2] (7.5k/15kHz numerology) | Further Extended Delay Spread (1.25kHz numerology) | 
0 | 0 | 0
30 | 30 | -1.5
150 | 150 | -1.4
310 | 310 | -3.6
370 | 370 | -0.6
1090 | 1090 | -7.0
12490 | 49960 | -10
12520 | 50080 | -11.5
12640 | 50560 | -11.4
12800 | 51200 | -13.6
12860 | 51440 | -10.6
13580 | 54320 | -17.0
27490 | 109960 | -20
27520 | 110080 | -21.5
27640 | 110560 | -21.4
27800 | 111200 | -23.6
27860 | 111440 | -20.6
28580 | 114320 | -27.0

## Slide 3: Test lists for mixed cell and dedicated PMCH
RAN4 considers to evaluate the tests as following.
The other test parameters are TBD in email discussion
Test number | Single carrier or CA | Subcarrier spacing | Antenna config | Bandwidth | Modulation order | Channel model | No. subframes for MBMS
1 | Mixed carrier PMCH | 1.25kHz | 1x2 | 10MHz | 16QAM 1/2 | New channel model | 8
2 | Mixed carrier PMCH | 7.5kHz | 1x2 | 10MHz | 16QAM 1/2 | New channel model | 8
3 | Mixed carrier PMCH | 1.25kHz | 1x2 | 10MHz | 64QAM 2/3 | New channel model | 8
4 | Dedicated PMCH | 1.25kHz | 1x2 | 10MHz | 16QAM 1/2 | New channel model | 10
5 | Dedicated PMCH | 1.25kHz | 1x2 | 10MHz | 64QAM 2/3 | New channel model | 10
6 | Dedicated PMCH | 15kHz | 1x2 | 3MHz | QPSK 1/3 | Existing channel model | 10
7 | Dedicated PMCH | 15kHz | 1x2 | 5MHz | 16QAM ½ | Existing channel model | 10
8 | Dedicated PMCH | 15kHz | 1x2 | 10MHz | 64QAM 2/3 | Existing channel model | 10

## Slide 4: PDSCH test parameters for unicast
For unicast PDSCH demodulation test with MBSFN awareness, extend the existing single carrier single PRB allocation test to the CA scenario with the increasd MBSFN subframes allocation of 80% as shown following page, where SCell is on the non-dedicated FeMBMS carrier.