## Slide 1: WF on NR Base Station emission mask
Agenda Item: 10.4.3.2
Document for: Approval
Source: Ericsson, ZTE
3GPP TSG-RAN WG4 #82bis Tdoc R4-1704354 Spokane, Washington, USA, 3-7 April, 2017

## Slide 2: Background
For legacy bands below 6 GHz, unwanted emissions for LTE are specified as UEM (i.e. band-centric), spanning the band plus 10 MHz on each side (ΔfUEM = 10 MHz)
Two contributions related to the BS unwanted emissions below 6 GHz were presented at RAN4#bis:
  [1] R4-1702837, "NR BS unwanted emission mask for below 6GHz" (ZTE Corporation).
    Proposes UEM principle for below 6GHz mask for NR
  [2] R4-1703094, "NR BS boundary between out-of-band and spurious domain below 6 GHz" (Ericsson).
    NR should be specified as UEM, defined with ΔfUEM = 40 MHz for bands wider than 100 MHz.

## Slide 3: Way-forward for NR unwanted emissions below 6 GHz
Use UEM principle (band-centric) for emissions below 6 GHz
For specific wider bands allowing wide RF channels, ΔfUEM can be larger than 10 MHz
  Investigate ΔfUEM larger than 10 MHz
  Study filter feasibility for AAS-type BS and the impact on ΔfUEM
The same emission levels as for LTE should be used within the frequency range (FDL_low– ΔfUEM) ~ (FDL_high+ΔfUEM).