## Slide 1: WF on mmW UE power class
Qualcomm Incorporated, Ericsson, Sony, Skyworks
3GPP TSG-RAN WG4#82 Bis
Spokane, USA, April 3rd-4th, 2017
R4-1704362
Document for: Approval

## Slide 2: Background
Output power capability defintion has been discussed for many meeting
Two proposals have been presented
  Specify UE power class with as TRP [3]
  Specify power class with EIRP with only maximum limit for TRP [1]
NR Band | Power class A |  |  |  | Power class B |  |  | 
 | EIRP |  | TRP |  | EIRP |  | TRP | 
 | Nominal | Tolerance | Nominal | Tolerance | Nominal | Tolerance | Nominal | Tolerance
X | 34 dBm | +2 /-6 dB | 23 dBm | +1 | 30 dBm | +2 /-6 dB | 19 dBm | +1
Y |  |  |  |  |  |  |  | 
Band | TRP Class 1 (dBm) | Tolerance (dB) | TRP Class 2 (dBm) | Tolerance (dB) | Maximum EIRP (dBm)
“28 GHz” | 20 dBm | ±2 |  |  | 43

## Slide 3: Way Forward
Agreement
  UE must be able to produce certain EIRP
  Powerclass definition includes upper limit for TRP which need to be met regardless of beamforming settings
Further details for power class definition are FFS

## Slide 4: Reference
[1] R4-1703044, NR mmWave UE power class, Qualcomm Incorporated
[2] R4-1703060, Power metrics for defintion of UE power classes, Ericsson, Sony
[3] R4-1703061, UE power classes for 28 GHz operation, Ericsson, Sony
[4] R4-1703064, NR – UE maximum output power in the context of TRP, EIRP and its beamforming capabilities for cmW and mmW ranges, InterDigital Communications
[5] R4-1703276, On Tx power requirement of mmWave UE, Sumitomo Elec. Industries, Ltd
[6] R4-1703876, On UE transmit power requirements for mmW, Qualcomm Incorporated