## Slide 1: WF on Maximum Channel Bandwidth
Qualcomm Incorporated, Vodafone, Dish
3GPP TSG-RAN WG4#82 Bis
Spokane, USA, April 3rd-4th, 2017
R4-1704412
Agenda : 10.3.1
Document for: Approval

## Slide 2: Background for Support of New Channel Bandwidths
Addition of new maximum channel bandwidths in a backwards compatible way should be allowed in a future release
  Legacy UEs should still be able to operate in a channel with the newly introduced bandwidth
  The gNB may configure a new CHBW that is not supported by legacy UEs but these UEs can still operate in this channel
  Handling of a the gNB configurable CHBW with CA by the UE that does not support the configurable CHBW needs to be supported in the specifications for forward compatibility
    RAN1 already agreed this [R1-1706615]
  gNBs will have to handle UEs that support the largest gNB configurable CHBW with CA such that legacy UEs can operate their UEMBW despite having limited CHBW
  All CHBW to be supported by UE shall be defined in the spec
    Support of Which CHBW is mandatory will be further discussed
MaxCHBW 400MHz
CHBW 312MHz
MaxCHBW400MHz
CHBW
200MHz
MaxCHBW 600MHz
MaxCHBW 600MHz
Rel.15
Future Release
Addition of
600MHz CHBW
gNB
Rel-15 UE
UEMBW = 600MHz
RFBW = 712MHz
CHBW 112MHz
MaxCHBW400MHz
CHBW
200MHz
UEMBW = 600MHz
RFBW = 712MHz
Rel-16 UE
UEMBW = 600MHz
NOTE: UE cannot operate a wider CHBW than BS is operating

## Slide 3: Agreements
Addition of new maximum channel bandwidths is allowed in future releases
  NR design should ensure forward compatibility, send LS to RAN1/2 to inform about this agreement
All defined channel bandwidths should be supportable by at least one type of UE and will be defined in the UE specs. Implementation of channel bandwidths in the specs will be done in order to minimize market fragmentation of UE.
FFS: Whether a fixed subset of all combinations of aggregations of potential Channel Bandwidths are specified for the BS, or whether the contiguous operated bandwidth is fully flexible for the BS, e.g. more granular than the minimum defined channel bandwidth. However a fixed subset will be tested.
The set of channel bandwidths for the UE and max Channel Bandwidth for the UE and BS, will be band and SCS specific and can be different for UL & DL
The maximum RF bandwidth supportable by BS can be larger than the maximum channel bandwidth

## Slide 4: Maximum channel bandwidth (CHBW) in Rel. 15
For bands below 6GHz
  100MHz maximum CHBW
For bands above 24GHz
  400MHz maximum CHBW
Whether different maximum channel bandwidths are defined for different SCS is FFS
  Maximum channel bandwidths for certain SCS can be smaller than the ones listed above but not larger
Not all UEs need to support the maximum channel bandwidth but the maximum channel bandwidth specified inUE specs shall not be lower than the maximum channel bandwidth specified in BS specs