## Slide 1
3GPP TSG-RAN WG4 #83 R4-1704511 Hangzhou, China, 15 - 19 May, 2017
Agenda item: 10.2.2 - NR-LTE band combinations proposals [NR_newRAT]
Document for: Approval
Working Procedure for LTE-NR combinations
KDDI Corporation

## Slide 2: Background
In RAN4#82-bis, several LTE-NR combinations (LNC) were proposed and RAN4 approved them.
In the combinations, not only 1CC (LTE) + 1CC (NR) combo but also multi-CC (LTE CA) + 1CC (NR) combo were included.
We propose RAN4 working procedure for LNCs.
We think prioritization is NOT an appropriate solution for RAN4 procedure.

## Slide 3: RAN4 history for CA
Considering CA working procedure, RAN4 took phased approach. Namely,
  In order to finalize certain CA combinations, specifications for all of fallback mode shall be finalized.
1UL-5DL CA
CA_1A-2A-3A-4A-5A
<Example>
1UL-4DL CA
CA_1A-2A-3A-4A
CA_1A-2A-3A-5A
…and so on
1UL-3DL CA
CA_1A-2A-3A
CA_1A-2A-4A
CA_1A-2A-5A … and so on
1UL-2DL CA
CA_1A-2A
CA_1A-5A
CA_1A-3A
CA_2A-3A
CA_1A-4A
… and so on
Base combination (5DL)
Fallback mode (2DL ~ 4DL)

## Slide 4: For LNC working procedure
For LNC (LTE-NR combinations) working procedure, RAN4 should adopt same approach as CA working procedure. Example can be found in the next slide.
For UL, up to 2CCs (LTE1CC + NR1CC) should be assumed in Rel.15.
LTE1CC
+
NR1CC
LTE2CC CA
+
NR1CC
LTE3CC CA
+
NR1CC
LTE4CC CA
+
NR1CC

## Slide 5: Example: [CA_1A-3A-20A-28A]+[NR: 3.3-4.2GHz]
Firstly, work for all of LTE 1CC + NR 1CC should be done; B1+NR, B3+NR, B20+NR, B28+NR.
Secondly, LTE 2CC + NR 1CC should be handled; CA_1A-3A+NR, CA_1A-20A+NR, CA_1A-28A+NR, …
Then, LTE3CC+NR1CC would be handled.
Finally, CA_1A-3A-20A-28A + NR could be discussed and finalized.

## Slide 6: Conclusion
As working procedure for LTE-NR combinations in RAN4,
Proposal#1: Prioritization should not be an appropriate solution. All combo should be handled by contribution driven.
Proposal#2: RAN4 should adopt same approach as CA working procedure.
Proposal#3: For UL, up to 2CCs (LTE1CC + NR1CC) should be assumed in Rel.15.