## Slide 1: WF on NR MU and test tolerance
CATR, Intel Corporation, Keysight Technologies, Rohde & Schwarz, Anritsu Corporation
3GPP TSG-RAN WG4 Meeting #83 R4-1704766
Hangzhou, China, May 15-19, 2017
Agenda item: 10.7.1
Document for: Approval

## Slide 2: Uncertainty budget calculation principle
Two stage for MU table:
Stage 1: the calibration of the absolute level of the DUT measurement results is performed by means of using a calibration antenna whose absolute gain is known at the frequencies of measurement
Stage 2: the actual measurement with the DUT as either the transmitter or receiver is performed.
The MU budget should comprise of a minimum 5 headings:
The uncertainty source,
Uncertainty value,
Distribution of the probability,
Divisor based on distribution shape,
calculated standard uncertainty (based on uncertainty value and divisor).

## Slide 3: Necessary MU elements for TX*
UID | Description of uncertainty contribution | Details in annex
Stage 2: DUT measurement |  | 
1 | Positioning misalignment | TBD
2 | Measure distance uncertainty | TBD
3 | Quality of quiet zone | TBD
4 | Mismatch in the Tx and Rx chain | TBD
5 | gNB emulator uncertainties | TBD
6 | Absolute antenna gain uncertainty | TBD
7 | Uncertainty of the RF power measurement equipment | TBD
8 | Phase curvature | 
9 | Repeatability | TBD
10 | Amplifier uncertainties | TBD
11 | Random uncertainty | 
Stage 1: Calibration measurement |  | 
12 | Impedance mismatch | TBD
13 | Reference antenna positioning misalignment | TBD
14 | Mismatch and insertion loss | TBD
15 | Quality of quiet zone | TBD
16 | Amplifier uncertainties | TBD
17 | Uncertainty of the Network Analyzer | TBD
17 | Reference antenna feed cable loss measurement uncertainty | TBD
18 | Uncertainty of an absolute gain/ radiation efficiency of the calibration antenna | TBD
19 | Positioning and pointing misalignment between the reference antenna and the receiving antenna | TBD
*Other MU elements are not precluded

## Slide 4: Descriptions of MU elements
Companies are encouraged to submit the details about the required MU elements (for TX and RX) for the RF baseline method including
The uncertainty source,
Uncertainty value,
Distribution of the probability,
Divisor based on distribution shape,
calculated standard uncertainty (based on uncertainty value and divisor).