## Slide 1: Optimization of UE capability signalling
Qualcomm
3GPP TSG-RAN WG4 Meeting #83 Hangzhou, China., 15 - 19 May 2017
R4-1705126

## Slide 2: Recent LTE UE capability optimizations from 2/2017 and 4/2017 RAN2 meetings

## Slide 3: eNB queries UE to report capability only for particular band combinations
Idea: Although 3GPP spec defines hundreds of CA band combinations, an operator has a limited number of bands in a given market/region.
  The eNB can request the UE to report UE capability only for the band combinations that the eNB supports.
  If UE supports e.g., Bx+By+Bz combination, the UE does not need to report the fallback band combinations e.g., Bx+By if the capability is the same as that of Bx+By+Bz.
  The UE may report the fallback combinations e.g., Bx+By if the capability is different than that of Bx+By+Bz.
RAN2 agreed the following Release 14 spec CRs following the idea above.
  2/2016: R2-1702399.
  4/2016: R2-1703927 (adding one more variant).
With these RAN2 enhancement, the oversizing UE capability issue is very unlikely to happen for LTE-only case without 5G-NR. See Case 2 in the example in the following slides for details.

## Slide 4: eNB queries UE to report capability only for particular band combinations
Example of using the optimization in two new RAN2 CRs.
  UE actual capability: supported BCs (3CC at maximum):
    1A+2A+3A and their fallback BCs (1A+2A, 2A+3A and 1A+3A). 1A+2A, 2A+3A and 1A+3A have different capabilities than 1A+2A+3A.
    4A+5A+6A and their fallback BCs with the same/different capabilities.
    7A+8A
  Case 1: eNB includes only skipFallbackCombinations in the UE capability enquiry message. UE reports:
    1A+2A+3A and skip fallback BCs indicating differentFallbackSupported
    4A+5A+6A and skip fallback BCs indicating differentFallbackSupported
    7A+8A

## Slide 5: eNB queries UE to report capability only for particular band combinations
Example of using the two new RAN2 CRs (continued).
  Case 2 (Big UE capability size reduction!): eNB includes diffFallbackCombReport only and eNB asks 1A+2A+3A in the UE capability enquiry message. UE reports:
    1A+2A+3A and its fallback BCs (1A+2A, 2A+3A and 1A+3A) for which supported UE capability is different from 1A+2A+3A
    UE does not report any other band combinations
  Case 3: eNB includes skipFallbackCombinations and diffFallbackCombReport in the UE capability enquiry message; eNB asks 1A+2A+3A in the UE capability enquiry message
    1A+2A+3A and its fallback BCs (1A+2A, 2A+3A and 1A+3A) for which supported UE capability is different from 1A+2A+3A
    4A+5A+6A and skip fallback BCs indicating differentFallbackSupported
    7A+8A

## Slide 6: Capability signalling after CA configuration

## Slide 7: Capability inquiry for per-CC gap
Capability inquiry procedure
  eNB configures CA and measurement objects
  eNB inquires UE per-CC gap capability
  UE provides per-CC gap capability
    CC requires legacy gap
    CC requires no gap
    CC requires interruption gap
Similar inquiry procedure can be applied for baseband feature that has dependency on CA configuration
  eNB configures CA SCells
  eNB inquires baseband capability for set of baseband features for configured CA
    Set of baseband features includes features that are supported by the eNB
  UE provides capability of inquired baseband features for configured CA
  Capability inquiry happens whenever eNB adds or removes SCell.