## Slide 1: WF on NR cell detection
Nokia, Alcatel-Lucent Shanghai Bell
3GPP TSG-RAN WG4 Meeting #83 R4-1705158
Hangzhou, China, 13 – 19 May 2017

## Slide 2: Simulation assumptions for NR cell detection
Parameter | Value
Carrier frequency | 4 GHz
PSS sequence type | Zhadoff-Chu, cyclically shifted M-sequence
SSS sequence type | LTE SSS sequence, scrambled M-sequence
Number of NR-PSS sequences | 3
Number of SSS sequences | 168, 336
PSS/SSS length | 127
PSS/SSS period | 10, 20, 40, 80, 160 ms
Sub-carrier spacing | 15 kHz
Channel model | CDL-C 100 ns scaling
UE speed | 30 km/h
PSS receiver algorithm | Single-shot time-domain correlator with thresholding
SSS receiver algorithm | Single-shot non-coherent exhaustive search with thresholding
False alarm probability | < 1 %

## Slide 3: Simulation assumptions for NR cell detection
Further assumptions:
  1 cell environment
  1 gNB Tx antenna
  2 UE Rx antennaes
  SNR level: -6 dB
Simulation results:
  Cell Detection delay.
  Companies should list false alarm rate.

## Slide 4: Way Forward
Interested companies are encouraged to provide simulation results for NR cell detection.
Initial results ready in RAN4 AH meeting in Qingdao.
Simulation assumptions can be adjusted if necessary.