## Slide 1: Way Forward on Spectral Utilization
Qualcomm, Nokia, Ericsson, [NTT Docomo], [Vodafone], [Samsung], [ZTE], [Intel]
3GPP TSG-RAN WG4#83 R4-1705207
Hangzhou, CHINA, 15 - 19 May, 2017
Agenda: 10.3.3

## Slide 2: Background
Spectral utilization has been discussed in many meetings and two techniques has been propsed, filtering and windowing
Both techniques have their merits but no conclusion has been reached whic one provides better overall performance
In TR 38.803 it is captured that RAN4 define independent Tx and Rx unit requirements and corresponding test setups allowing different implementations

## Slide 3: WF on maximum spectral utilization <6 GHz
 | CH BW [MHz] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SCS [kHz] | 5 |  | 10 |  | 15 |  | 20 |  | 30 |  | 40 |  | 60 |  | 80 |  | 100 | 
 | NRB | Y [%] | NRB | Y [%] | NRB | Y [%] | NRB | Y [%] | NRB | Y [%] | NRB | Y [%] | NRB | Y [%] | NRB | Y [%] | NRB | Y [%]
15 | 25 | 90.0 | 52 | 93.6 | 79 | 94.8 | 106 | 95.4 | 161 | 96.6 | 216 | 97.2 | N.A. | N.A | N.A | N.A | N.A | N.A
30 | [12] | [86.4] | 25 | 90.0 | 38 | 91.2 | 52 | 93.6 | 79 | 94.8 | 106 | 95.4 | 162 | 97.2 | 217 | 97.7 | 273 | 98.3
60 | N.A | N.A | N.A | N.A | N.A | N.A | 25 | 90.0 | 38 | 91.2 | 52 | 93.6 | 80 | 96.0 | 107 | 96.3 | 135 | 97.2
Spectral utilization does not exceed the values in table below
Note: The bandwidths here are examples; a subset may be selected for the final set of BW. Supported bandwidths is a separate discussion not part of this WF.

## Slide 4: WF on maximum spectral utilization > 24 GHz
 | 50 MHz |  | 100 MHz |  | 200 MHz |  | 400 MHz | 
 | NRB | Y [%] | NRB | Y [%] | NRB | Y [%] | NRB | Y [%]
60 KHz | 67 | 96.48 | 136 | 97.2 | 275 | 99 | NA | NA
120 KHz | 33 | 95.04 | 67 | 96.48 | 137 | 98.64 | 276 | 99.36
240 KHz | 16 | 92.16 | 33 | 95.04 | 68 | 97.92 | 137 | 98.64
Maximum Spectral utilization is considered for values in table below
Companies are encouraged to study feasibility based on values below especially for cases with Y > 98 %
Note: The bandwidths here are examples; a subset may be selected for the final set of BW. Supported bandwidths is a separate discussion not part of this WF.