## Slide 1: WF on Multi-node tests
Qualcomm, Ericsson, Huawei, HiSilicon, Nokia, Alcatel-Lucent, Shanghai Bell, Skyworks, AT&T, T-Mobile USA, Verizon, Deutsche Telekom, Vodafone, [US Cellular]
3GPP TSG-RAN WG4 #82bis
May 15th – 19th, 2017
Hangzhou, China
R4- 1705475

## Slide 2: Background information
A way forward on multi-node tests was approved in RAN4 #82bis (R4-1704409)
Most of the issues were resolved, with only the following items to be concluded:
  Receiver signal levels and SIR
  Traffic Types
  Detail of evaluation metrics
In the following slides we provide a way forward capturing an overall compromise for the open items

## Slide 3: Receiver signal levels and SIR
Two test levels are defined, corresponding to received interference signal levels above and below ED (Link A-B), respectively:
  Above ED configuration:
    AP-STA: -57dBm, AP-eNB: -67dBm, eNB-STA: -67dBm. => SIR: 10dB
  Below ED configuration
    AP-STA: -70dBm, AP-eNB: -80dBm, eNB-STA: -80dBm => SIR: 10dB
Same levels should be applied when Wi-Fi is aggressor and LAA is Victim

## Slide 4: Traffic Types
The following scenarios are considered
Tests with voice traffic on the aggressor link will be made only if the LAA eNB supports voice. If it doesn’t support voice, test 3 won’t be performed and tests 2 and 4 will have only Best Effort in the aggressor link
Throughput tests |  | 
Scenario | Traffic in victim link | Traffic in aggressor link
1 | Best effort | Best effort
2 | Best effort | Best effort + Voice
Outage tests |  | 
Scenario | Traffic in victim link | Traffic in aggressor link
3 | Voice | Voice
4 | Voice | Best effort + Voice

## Slide 5: Evaluation metrics
Performance metrics
  Throughput tests: normalized throughput
  Outage tests: FFS (options: MOS score and/or Jitter and/or outage)
The evaluation process should assess the following percentile points of the performance distribution
  50%