## Slide 1: WF on NB-IoT additional spectrum emission mask
Neul, Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #83
Hangzhou, China 15 – 19 May 2017
R4-1705868

## Slide 2: Background
In guard-band deployment, UE has no knowledge of its frequency location relative to the LTE channel edge;
New network signalling may be needed to inform the UE that a different/tighter spectrum emission mask (SEM) is imposed compared with the general SEM;
The signalling mechanism for additional SEM has already been defined by RAN2 in Rel-13 TS 36.331.
References
[1] R4-1705579 NB-IoT Additional SEM
[2] TS 36.331 v13.5.0

## Slide 3: Example Case: Guard-band deployment in a 10 MHz LTE channel
Figure 1: SEMs for an NB-IoT carrier deployed in the guard-band of a 10MHz LTE channel. The four valid frequency locations are shown by different colors.
Figure 2: Zoomed-in SEMs, where the interceptions of the SEMs are clearly shown.

## Slide 4: Example additional SEM
modification

## Slide 5: Proposals
Evaluate and, if appropriate, specify new network signalling value(s) for NB-IoT additional SEM for guard-band deployment in Rel-14;
At least the following aspects are considered:
  - Potential deployment scenarios (including different LTE channel BWs and NB-IoT carrier locations);
  - The definition of new SEM(s);
  - Potential A-MPR to assist UEs to meet the A-SEM;
  - Potential impact on coexistence (e.g. base station blocking requirements);
  - NS message numbering
  - Supported RF bands;
The following case is considered as a priority:
  - a NB-IoT carrier is deployed in the left-hand side or right-hand side guard-band of a 10 MHz LTE carrier with a gap of 105 kHz between the NB-IoT RB and the LTE edge RB