## Slide 1: WAY FORWARD ON REL-14 CAT M2 REFSENS
Ericsson, Sony, Qualcomm, KDDI
3GPP TSG-RAN WG4 Meeting #83
Hangzhou, China, 15-19 2017
R4-1705875

## Slide 2: Background
A Rel-14 WI on ‘Further Enhanced MTC for LTE’ was approved at RAN#72 with core part completion due by March 2017 (RAN#75) and the RAN4 performance part by September 2017 (RAN#77) [1].
It is noticed that the current R-13 Cat-M1 REFSENS is converged result after agreement [2][4][5]
In WI [1], the following bands shall be considered with high priority for defining any RAN4 band specific requirement within Release 14: 1, 2, 3, 4, 5, 7, 8, 11, 12, 13, 18, 19, 20, 21, 25, 26, 27, 28, 31, 39, 40, 41 and 66.

## Slide 3: WAY FORWARD
The REFSENS value for rel-13 CAT-M2 eMTC will be added with bracket
The REFSENS value in bracket for rel-13 CAT-M2 eMTC will be based on R13 CAT-M1 eMTC in [3] with scaling factor considered below respect to CAT-M1 REFSENS:
  For 5MHz channel in FDD/TDD and HD-FDD ,
    using the scaling factor: +10*log10(24 PRB/6 PRB)=6 dB
  For 3MHz channel in FDD/TDD and HD-FDD
    using the scaling factor: +10*log10(15 PRB/6 PRB)= 4 dB
Additional CR in further meeting is needed to remove bracket or modify value

## Slide 4: Reference
[1] RP-170532, “Further Enhanced MTC for LTE”
[2] R4-158435, UE receiver requirements for Rel-13 MTC
[3] 36.101 R14.3.0
[4] R4-156923; Way forward for rel-13 eMTC REFSENS, Sony; Ericsson, RAN4#76bis
[5] R4-156247; Way forward for rel-13 eMTC REFSENS, Sony, RAN4#76bis