## Slide 1: Proposals on concluding the MIMO OTA WI
CATR, Intel Corporation, Huawei, CMCC, Rohde & Schwarz, Keysight, ATR, Spirent, Bluetest, NTT DOCOMO
3GPP TSG-RAN WG4 Meeting #83 R4-1705935
Hangzhou, China, May 15-19, 2017
Agenda item: 7.11.1
Document for: Approval

## Slide 2: Background
CATR shares the harmonization results[1] and lab alignment results[9]
Measurement uncertainty of each harmonization system is also provided by CATR [2-4]
Some analysis results are presented in [5-8]

## Slide 3: Performance lab alignment
Proposals for performance part:
P1: Due to the potential alignment between MPAC labs, group should continue the performance requirement phase for MPAC
P2: Select the alignment results from CATR as the reference, suggest Lab1 and Lab2 to retest PAD devices for lab alignment activity, as defined in 10.4 of TR37.977
P3: A work plan to progress the alignment activity and to root-cause the observed issues shall be defined and led by the MPAC solution provider companies
P4: The PADs and reference dipoles are passed from Lab3 to Lab2, then to Lab1 to enable the investigation

## Slide 4: Performance requirement work
Proposals for performance part:
P5: Given the capability of RTS method and the need to utilize any commercially available devices for collecting the TRMS data, the MPAC should be the single methodology for MIMO performance requirement

## Slide 5: harmonization activity (MPAC/RC+CE)
P6: For the TDD bands tested in the MPAC/RC+CE harmonization, the harmonization cost varies between 0.37 and 0.60 dB. This harmonization cost is within the lowest harmonization target for all TDD bands considering the statistical significance. Because only 3 devices were used to determine the offsets, harmonization between MPAC and RC+CE for Bands 38 and 41 should be further investigated. Testing 5 more devices in the chosen TDD bands in Lab3 can help to evaluate the harmonization offsets and the harmonization cost for TDD.
P7: For all FDD bands tested in the MPAC/RC+CE harmonization, the harmonization cost varies between 1.19 and 2.58 dB; some bands exceed their highest harmonization bound and, therefore, harmonization between MPAC and RC+CE cannot be confirmed for all FDD bands based on the results available from the harmonization testing campaign.
P8: The potential to harmonize in FDD has been observed by isolating devices which have contributed to higher residual errors, particularly LNA-active devices, defining the related applicability criteria, and investigating more suitable RC+CE settings and harmonization formulas.

## Slide 6: harmonization activity (MPAC/RTS)
P9: For the FDD bands tested in the MPAC/RTS harmonization, the harmonization cost varies between 0.5 and 0.92 dB. This harmonization cost is within the harmonization target for all bands and, therefore, harmonization between MPAC and RTS for Bands 13, 5, 3, and 7 can be confirmed.
P10: Considering the positive outcome of the MPAC/RTS harmonization analysis, the following applicability criteria for the MPAC/RTS harmonization are proposed based on the current understanding of the RTS methodology capabilities:
  The harmonized RTS system is a two probe system capable of measuring devices with two Rx antennas. Devices with more Rx antennas are not supported
  The RTS method is only applicable to devices which do not change their antenna pattern in response to the radio environment
  The RTS method requires device support for the antenna test function (ATF) defined in TR 36.978. The ATF access of devices depends on the support of chip vendors
  There are two methods defined for ATF access, L3 signalling or a vendor-supplied device app. The devices used for harmonization were all modified to install the special ATF application. Harmonization has been confirmed using devices with the special ATF application. Harmonization for unmodified devices using the L3 access has not been confirmed.
  RTS is harmonized for FDD bands. TDD harmonization has not been evaluated.
  Harmonization measurements for RTS were performed with correlation based channel models; harmonization and channel model validation limits would need to be confirmed for geometric based channel models

## Slide 7: Next Steps
It is recommended to consider an extension of the work item to finalize the performance aspects identified in slides #3 and #4
It is recommended to consider a new harmonization activity within the scope identified in slide #5 for TDD and FDD bands as part of the extension of the work item
RTS will investigate TDD and geometric channel model harmonization and support for >2 Rx UE receivers

## Slide 8: Reference
R4-1704750, “MIMO OTA harmonization testing results (part 3),” CATR, 3GPP RAN4 #83, May 2017
R4-1705191, “Measurement uncertainty of the RTS system for harmonization test campaign,” CATR, 3GPP RAN4 #83, May 2017
R4-1705192, “Measurement uncertainty of the MPAC system for harmonization test campaign,” CATR, 3GPP RAN4 #83, May 2017
R4-1705211, “Measurement uncertainty of the RC+CE system for harmonization test campaign,” CATR, 3GPP RAN4 #83, May 2017
R4-1702254, “Views on concluding the MIMO OTA Work Item,” Intel Corporation, 3GPP RAN4 #82, February 2017
R4-1704657, “MIMO OTA email discussion,” Intel Corporation, Bluetest, 3GPP RAN4 #83, May 2017
R4-1704661, “Harmonization analysis,” Intel Corporation, CATR, 3GPP RAN4 #83, May 2017
R4-1704578, “Analysis of Harmonization Results,” Rohde & Schwarz, 3GPP RAN4 #83, May 2017
R4-1705313 , “ Measurement results of PAD devices for lab alignment,” CATR, 3GPP RAN4 #83, May 2017