## Slide 1: WF on CRS-IM capability and assistance signalling
Qualcomm, Intel, CATT
3GPP TSG-RAN WG4 Meeting #83 Hangzhou, China., 15 - 19 May 2017
R4-1706031

## Slide 2: Background
Rel-13 CRS-IM capability signaling (crs-InterfMitigationTM1toTM9)
  Indicates whether the UE supports CRS interference mitigation (IM) while operating in the following transmission modes (TM): TM 1, TM 2, …, TM 8 and TM 9. The UE shall not include the field if it does not support CRS IM in TMs 1-9. If the field is present, the UE supports CRS-IM on at least one arbitrary downlink CC for up to crs-InterfMitigationTM1toTM9-r13 downlink CC CA configuration. The UE signals crs-InterfMitigationTM1toTM9-r13 value to indicate the maximum crs-InterfMitigationTM1toTM9-r13 downlink CC CA configuration where UE may apply CRS IM. For example, the UE sets “crs-InterfMitigationTM1toTM9-r13 = 3” to indicate that the UE supports CRS-IM on at least one DL CC for supported non-CA, 2DL CA and 3DL CA configurations. The UE supporting the crs-InterfMitigationTM1toTM9-r13 capability shall also support the crs-InterfHandl-r11 capability.
Rel-13 CRS assistance signaling
  eNB provide PCID, number of CRS ports and MBSFN subframe configuration for all neighbor potential neighbor cells
  CRS assistance signaling can be provided for both PCell and SCells.

## Slide 3: Background
Rel-14 Enhanced CRS-IM feature list
  #1: PDSCH non-colliding CRS-IM receiver for 2RX and 4 CRS APs
  #2: PDSCH non-colliding CRS-IM receiver for 4RX and 2 CRS APs
  #3: PDSCH non-colliding CRS-IM receiver for 4RX and 4 CRS APs
  #4: Type A CCIM receiver for 2RX and 4 CRS APs for DL Control Channels
  Other feature can be added depending on further RAN4 discussion
RAN4 need to define capability signaling that covers all CRS-IM features
It would be desirable to reduce CRS assistance signaling overhead

## Slide 4: WF on UE capability signaling
Introduce the following UE capabilities signalling
  #1: CRS-IM capability
    UE can indicate per-UE 1 bit CRS-IM capability if it supports at least one of features
      Rel-14 CRS-IM
      Rel-13 CRS-IM
      Rel-13 DL Control Channel IM (CCIM)
      on at least one CC in at least one CA configuration
  #2: CRS-IM + CRS port blind detection capability
    UE can indicate per-UE 1 bit CRS-IM with CRS port blind detection capability if it supports at least one of features
      Rel-14 CRS-IM
      Rel-13 CRS-IM
      Rel-13 DL Control Channel IM (CCIM)
    on at least one CC in at least one CA configuration and
    and it can perform neighbor cells CRS port blind detection on any CC that these features are applied to

## Slide 5: WF on UE capability signaling
Capabilities signaling is applied at least from Rel-14
Working assumption (TBC in RAN4 #84):
  Capabilities signaling defined for Rel-14 should be applied to both Rel-13 and Rel-14 UEs supporting the features
    Rel-14 CRS-IM
    Rel-13 CRS-IM
    Rel-13 DL Control Channel IM (CCIM)

## Slide 6: WF on CRS assistance signaling
Request RAN2 to introduce simplified Rel-14 CRS assistance signaling
  Option 1:
    1 bit flag to indicate that neighbor cells have same configuration as serving cell for the number of CRS ports and/or MBSFN SF configuration
  Option 2:
    1 bit flag to indicate that number of CRS ports in neighbor cells is same as serving cell
    1 bit flag to indicate that MBSFN SF configuration in neighbor cells is same as serving cell
  Note: simplified CRS assistance signaling is provided on a per CC basis

## Slide 7: WF on procedure with optimized CRS assistance signaling
If network provides “full” Rel-13 CRS assistance signaling for one or more neighboring cells then UE should assume that the related cells use the parameters provided in the CRS assistance message
If network provides “simplified” Rel-14 CRS assistance signalling with bit = 1
  UE with CRS-IM capability #1 can assume that all neighboring cells except cells with Rel-13 CRS assistance signaling have same configuration as serving cell in terms of number of CRS APs and MBSFN subframe configuration
  UE with CRS-IM capability #2 can assume that all neighboring cells except cells with Rel-13 CRS assistance signaling have same configuration as serving cell in terms of MBSFN subframe configuration
If network provides “simplified” Rel-14 CRS assistance signalling with bit = 0, UE should not make any additional assumptions on the neighboring cell configuration