## Slide 1: WF for test scenario for performance requirement for FeMBMS
Ericsson, Qualcomm, [Huawei], [Intel]
3GPP TSG-RAN WG4 Meeting #83 R4-1706035 Hangzhou, China, 15th-19th May, 2017
Document Type: Approval

## Slide 2: Channel model
It’s proposed that subcarrier spacing 15kHz and 7.5kHz tests reuse the existing MBMS channel model defined in TS 36.101 Table B.2.6-1. For subcarrier spacing 1.25kHz it’s proposed to define a new channel model as following.
Maximum Doppler frequency [5Hz] |  | 
Relative Delay [ns] |  | Relative Mean Power [dB] (1.25k/7.5k/15kHz numerology)
Extended Delay Spread [2] (7.5k/15kHz numerology) | Further Extended Delay Spread (1.25kHz numerology) | 
0 | 0 | 0
30 | 30 | -1.5
150 | 150 | -1.4
310 | 310 | -3.6
370 | 370 | -0.6
1090 | 1090 | -7.0
12490 | 49960 | -10
12520 | 49990 | -11.5
12640 | 50110 | -11.4
12800 | 50270 | -13.6
12860 | 50330 | -10.6
13580 | 51050 | -17.0
27490 | 109960 | -20
27520 | 109990 | -21.5
27640 | 110110 | -21.4
27800 | 110270 | -23.6
27860 | 110330 | -20.6
28580 | 111050 | -27.0

## Slide 3: Test proposals for PMCH demodulation
Define the following tests for FeMBMS/Unicast-mixed cell for PMCH demodulation
Cell type | Test number | Bandwidth | FRC | PMCH Reference Channel | MBSFN Subframe Subcarrier Spacing | Propagation condition | Correlation Matrix and antenna | No. subframes for FeMBMS | Reference value |  | MBMS UE Category
 |  |  |  |  |  |  |  |  | BLER (%) | SNR(dB) | 
Pcell |  | 10 MHz |  | No PDSCH No PMCH | N/A | EPA5 | 1x2 low | N/A | N/A | N/A | 
FeMBMS/Unicast-mixed SCell Non-PCell (Note 1) | 1 | 10 MHz | R.81-1 FDD | 16QAM 1/2 | 1.25 kHz | New MBSFN Channel w/ >100us delay spread | 1x2 low | 8 | 1 | TBD | ≥1
 | 2 | 10 MHz | R.81-2 FDD | 64QAM 2/3 | 1.25 kHz |  |  |  |  | TBD | ≥2
 | 3 | 10 MHz | R.81-3 FDD | 16QAM 1/2 | 7.5 kHz | MBSFN channel model (Table B.2.6-1) |  |  |  | TBD | ≥1
Note 1: Non-PCell refers to SCell for a UE supporting both PMCH and unicast PDSCH reception from the FeMBMS/Unicast-mixed cell. Otherwise, Non-Pcell refers to non-serving cell. |  |  |  |  |  |  |  |  |  |  | 

## Slide 4: Test proposals for PMCH demodulation
Define the following tests for MBMS-dedicated cell for PMCH demodulation
Applicability rule for test 5 and 6 is FFS
Cell type | Test number | Bandwidth | FRC | PMCH Reference Channel | MBSFN Subframe Subcarrier Spacing | Propagation condition | Correlation Matrix and antenna | No. subframes for FeMBMS | Reference value |  | MBMS UE Category
 |  |  |  |  |  |  |  |  | BLER (%) | SNR(dB) | 
Pcell |  | 10 MHz |  | No PMCH, No PDSCH | N/A | EPA5 | 1x2 low | N/A | N/A | N/A | 
MBMS-dedicated cell | 1 | 10 MHz | R.82-1 FDD | 16QAM 1/2 | 1.25 kHz | New MBSFN Channel w/ >100us delay spread | 1x2 low | 10 | 1 | TBD | ≥1
 | 2 | 10 MHz | R.82-2 FDD | 64QAM 2/3 | 1.25 kHz |  |  |  |  | TBD | ≥2
 | 3 | 10 MHz | R.82-3 FDD | 16QAM 1/2 | 7.5 kHz | MBSFN channel model (Table B.2.6-1) |  |  |  | TBD | ≥1
 | 4 (Note 1) | 10 MHz | R.82-6 FDD | 16QAM 1/2 | 15 kHz |  |  |  |  | TBD | ≥1
 | 5 (Note 1) | 5 MHz | R.82-5 FDD | 16QAM 1/2 | 15 kHz |  |  |  |  | TBD | ≥1
 | 6 (Note 1) | 3 MHz | R.82-4 FDD | QPSK 1/3 | 15 kHz |  |  |  |  | TBD | ≥1
Note 1: UEs passing the legacy MBMS/Unicast-mixed cell related cases defined in TS 36.101 section 10 can skip these tests. |  |  |  |  |  |  |  |  |  |  | 

## Slide 5: Test proposal for PDSCH unicast demodulation
For unicast PDSCH demodulation test with MBSFN awareness, extend the existing single carrier single PRB allocation test 8.2.1.1.4 in TS36.101 to the CA scenario with the increased MBSFN subframe allocation of 80%, where SCell is FeMBMS/Unicast-mixed cell. A UE passing the new test can skip existing 8.2.1.1.4 test.
To use FRC R.29-1 FDD in the next pages

## Slide 6: FRCs for FeMBMS/Unicast-mixed cell
Parameter | PMCH |  |  | 
 | Unit | Value |  | 
Reference channel |  | R.81-1 FDD | R.81-2 FDD | R.81-3 FDD
Subcarrier spacing | KHz | 1.25 | 1.25 | 7.5
Channel bandwidth | MHz | 10 | 10 | 10
Allocated resource blocks |  | 50 | 50 | 50
Allocated subframes per Radio Frame(Note1) |  | 8 | 8 | 8
Modulation |  | 16QAM | 64QAM | 16QAM
Target Coding Rate |  | 1/2 | 2/3 | 1/2
Information Bit Payload (Note 2) |  |  |  | 
For Sub-Frames 1,2,3,4,6,7,8,9 | Bits | 11448 | 25456 | 12960
For Sub-Frames 0,5 |  | N/A | N/A | N/A
Number of Code Blocks per Sub-Frame (Note 3) |  | 2 | 5 | 3
Binary Channel Bits Per Subframe |  |  |  | 
For Sub-Frames 1,2,3,4,6,7,8,9 | Bits | 24000 | 36000 | 25200
For Sub-Frames 0,5 |  | N/A | N/A | N/A
MBMS UE Category |  | ≥ 2 | ≥ 2 | ≥ 2
Note 1: For FDD mode, up to 8 subframes (#1/2/3/4/6/7/8/9) are available for MBMS, in line with TS 36.331. Note 2: Zero OFDM symbols are reserved for PDCCH; and no CRS allocated as per TS 36.211. Note 3: If more than one Code Block is present, an additional CRC sequence of L = 24 Bits is attached to each Code Block (otherwise L = 0 Bit). |  |  |  | 
MBSFN RS EPRE is 3dB and 10.8dB lower than CRS EPRE for 7.5kHz and 1.25kHz subcarrier spacing, respectively

## Slide 7: FRCs for MBMS-dedicated cell
Parameter | PMCH |  |  |  |  |  | 
 | Unit | Value |  |  |  |  | 
Reference channel |  | R.82-1 FDD | R.82-2 FDD | R.82-3 FDD | R.82-4 FDD | R.82-5 FDD | R.82-6 FDD
Subcarrier spacing | KHz | 1.25(Note 2) | 1.25(Note 2) | 7.5(Note 2) | 15(Note 3) | 15(Note 3) | 15(Note 3)
Channel bandwidth | MHz | 10 | 10 | 10 | 3 | 5 | 10
Allocated resource blocks |  | 50 | 50 | 50 | 15 | 25 | 50
Allocated subframes per Radio Frame(Note1) |  | 10 | 10 | 10 | 10 | 10 | 10
Modulation |  | 16QAM | 64QAM | 16QAM | QPSK | 16QAM | 64QAM
Target Coding Rate |  | 1/2 | 2/3 | 1/2 | 1/3 | 1/2 | 2/3
Information Bit Payload (Note 2) |  |  |  |  |  |  | 
For Sub-Frames 0,1,2,3,4,5,6,7,8,9 | Bits | 11448 | 25456 | 12960 | 1064 | 4968 | 19848
Number of Code Blocks per Sub-Frame (Note 4) |  | 2 | 5 | 3 | 1 | 1 | 4
Binary Channel Bits Per Subframe |  |  |  |  |  |  | 
For Sub-Frames 0,1,2,3,4,5,6,7,8,9 | Bits | 24000 | 36000 | 25200 | 3060 | 10200 | 30600
MBMS UE Category |  | ≥ 2 | ≥ 2 | ≥ 2 | ≥ 1 | ≥ 1 | ≥ 2
Note 1: For FDD mode, all 10 subframes are available for MBMS, in line with TS 36.331. Note 2: Zero OFDM symbols are reserved for PDCCH; and no CRS allocated as per TS 36.211. Note 3: 2 OFDM symbols are reserved for PDCCH; and reference signal allocated as per TS 36.211. Note 4: If more than one Code Block is present, an additional CRC sequence of L = 24 Bits is attached to each Code Block (otherwise L = 0 Bit). |  |  |  |  |  |  | 
MBSFN RS EPRE is 0dB, 3dB and 10.8dB lower than CRS EPRE for 15kHz, 7.5kHz and 1.25kHz subcarrier spacing, respectively

## Slide 8: FRC for PDSCH demod with 8 MBSFN subframes
Parameter | Unit | Value
Reference channel |  | R.29-1 FDD (MBSFN)
Channel bandwidth | MHz | 10
Allocated resource blocks |  | 1
MBSFN Configuration (Note 4) |  | 111111
MBSFN Configuration-r14 (Note 5) |  | 11
Allocated subframes per Radio Frame |  | 1
Modulation |  | 16QAM
Target Coding Rate |  | 1/2
Information Bit Payload |  | 
For Sub-Frames 4,9 | Bits | 0 (MBSFN)
For Sub-Frame 5 | Bits | N/A
For Sub-Frame 0 | Bits | 256
For Sub-Frame 1,2,3,6,7,8 | Bits | 0 (MBSFN)
Number of Code Blocks per Sub-Frame (Note 3) |  | 
For Sub-Frames 4,9 |  | 0 (MBSFN)
For Sub-Frame 5 |  | N/A
For Sub-Frame 0 |  | 1
For Sub-Frame 1,2,3,6,7,8 |  | 0 (MBSFN)
Binary Channel Bits Per Sub-Frame |  | 
For Sub-Frames 4,9 | Bits | 0 (MBSFN)
For Sub-Frame 5 | Bits | N/A
For Sub-Frame 0 | Bits | 552
For Sub-Frame 1,2,3,6,7,8 | Bits | 0 (MBSFN)
Max. Throughput averaged over 1 frame | kbps | 25.6
UE Category |  | ≥ 1
Note 1: 2 symbols allocated to PDCCH in non-MBSFN subframes Note 2: Reference signal, synchronization signals and PBCH allocated as per TS 36.211 [4]. Note 3: If more than one Code Block is present, an additional CRC sequence of L = 24 Bits is attached to each Code Block (otherwise L = 0 Bit). Note 4: MBSFN Subframe Allocation as defined as MBSFN-SubframeConfig IE in [7], one frame with 6 bits is chosen for MBSFN subframe allocation Note 5: MBSFN Subframe Allocation as defined as MBSFN-SubframeConfig-v14xy IE in [7], one frame with 2 bits is chosen for MBSFN subframe allocation |  |