## Slide 1: WF on band definition for 3.3-4.2 GHz
NTT DOCOMO, INC., Softbank, Intel, Qorvo, KDDI, Nokia, NEC
3GPP TSG-RAN WG4 #83 Meeting Hangzhou, China, 15 – 19 May, 2017
R4-1706053

## Slide 2: Background on 3.3-4.2 GHz
There is an agreement of three options for the band definition of 3.3-4.2 GHz [1]
  Option 1: To specify two different bands below with a note indicating that “A UE supporting Band X shall also support Band Y and vice versa”.
    Band X: 3.3-3.8 GHz
    Band Y: 3.6-4.2 GHz *No additional switch loss is assumed.
  Option 2: To specify 3.3-4.2 GHz as a single band.
  Option 3: Option 1+2
It is understood that the band definition (Option 1 or 2) itself doesn’t impact UE implementation.
  More specifically, for example, even with Option 1, one PA implementation is still possible. Conversely, even with Option 2, two PA’s implementation is still allowed in some UE’s.
Band X
Band Y
Band Z
3.3
3.8
3.6
4.2
4.2
3.3

## Slide 3: Way forward
Specify a single band of 3.3-4.2 GHz i.e., Option 2 for simpler specification
No limitation should be specified for DL side in the entire band including intra-band non-contiguous DL CA
How to address implementation challenges for UL side is FFS for the next meeting

## Slide 4: References
[1] R4-1704218, “WF on 3.3-4.2 GHz and 4.4-4.99 GHz NR spectrum”, NTT DOCOMO, INC., Intel, Qualcomm, Qorvo, Skyworks, Ericsson