## Slide 1: WF on supported channel bandwidth and SCS
R4-1706055
Ericsson, …

## Slide 2: Summary of agreements
Frequency range | SCS (kHz) | Min CHBW (MHz) | Max CHBW (MHz)
Range 1 | 15 | 5 | 50
Range 1 | 30 | Option 1: 5MHz Option 2: 10MHz | 100
Range 1 | 60 | Option 1: 10MHz Option 2: 20MHz | 100MHz
Range 2 | 60 | 50 | 200
Range 2 | 120 | 50 | 400MHz
NOTE: These agreements and the following open issues agree to the data channel, not the PSS/SSS

## Slide 3: Open issues (below 6GHz)
30khz SCS minimum bandwidth 5 or 10MHz
  Issues to consider:
    5MHz / 30khz SS cannot be supported currently
      However 15khz SCS for SS and 30khz for data might possibly be supported
    Low spectral utilization for combination of 5Mhz and 30k SCS
60khz SCS minimum bandwidth 10 or 20MHz
  Issues to consider:
    Low spectral utilization for combination of 10Mhz and 60k SCS
    Likely URLLC deployment scenarios in LTE reframing band that need 60k SCS

## Slide 4: Way forward (below 6 GHz)
100MHz maximum CHBW for 60khz SCS
UE RF and performance requirements for 200MHz aggregated bandwidth should be introduced at least for Rel.15 NSA scenario
  UE category supporting 200MHz aggregated bandwidth will be introduced
  CA configuration is FFS (e.g. 100MHz x 2 continuous CCs)

## Slide 5: Way forward (above 24GHz)
400 MHz maximum channel bandwidth for 120khz SCS
UE RF and performance requirements for 800MHz aggregated bandwidth should be introduced at least for Rel.15 NSA scenario.
  UE category supporting 800MHz aggregated bandwidth will be introduced
  CA configuration is FFS (e.g. 400MHz x 2 continuous CCs)
  Testability of UE demodulation performance requirements is FFS