## Slide 1: WF on mmW ACLR and ACS
Qualcomm Incorporated, Huawei
R4-1706063
3GPP TSG-RAN WG4 RAN4 #83
Hangzhou, China, May 25th-19th, 2017

## Slide 2: Background information - 1
During NR SI, RAN4 conducted adjacent channel coexistence study for NR mmW with the following conclusions captured in TR 38.802:
 | Frequency Range |  | 
 | 30GHz | 45GHz | 70GHz
BS ACLR [dBc] | 27.5 | 25.5 | 23.5
BS ACS [dBc] | 23.5 | 22.5 | 21.5
UE ACLR [dBc] | 17 | 16 | 15
UE ACS [dBc] | 22.5 | 21.5 | 20.5

## Slide 3: Background information - 2
The main assumptions under which the requirements were derived are the following:
  Base Station operating in Indoor, Dense Urban and Urban Macro deployments with corresponding powers and antenna configurations
  User Equipment (UE):
    Conducted power: 23dBm
    Maximum EIRP: 34dBm

## Slide 4: Way forward on BS and UE ACLR
BS ACLR
  28dBc for 30GHz frequency range
  26dBc for 45GHz frequency range
  The absolute limits for ACLR values corresponding to different BS classes are FFS
UE ACLR
  17dBc for 30GHz frequency range
  16dBc for 45GHz frequency range
  The above ACLR are meant for a UE power class corresponding to the UE assumptions described in slide 3
  The absolute limits for ACLR values corresponding to low output power are FFS

## Slide 5: Way forward on BS and UE ACS
For mmW specifications the bandwidths of wanted and unwanted signals are assumed to be the same
BS ACS:
  24dBc for 30GHz frequency range
  23dBc for 45GHz frequency range
UE ACS
  23dBc for 30GHz frequency range
  22dBc for 45GHz frequency range