## Slide 1: 3GPP TSG-RAN WG4 Meeting #83
Ericsson, Qualcomm, Huawei
Transient time for sTTI
R4-1706098

## Slide 2: Background
Contributions on sTTI transient time have been discussed in RAN4#82b and RAN4#83:
  R4-1705570: Transient time for sTTI ON/OFF mask, Qualcomm
  R4-1705186: UE ON/OFF time mask for all use cases, Huawei, Hi-Silicon
  R4-1703840, Performance implication of UL ON/OFF time mask on sTTI operation, Ericsson
Current proposals for transient time for sTTI:
  10us (excluding CBW of 1.4MHz).
  5us

## Slide 3: Agreement
Companies are encouraged to provide UL receiver performacne results assuming linear model in dB for transient period.
  Typical UE performance should be considered as reference: [4]% EVM modelled as [28] dB AWGN noise
  The slope of the linear dB model is 23 dBm to -50 dBm in 10 usec. This slope shall be maintained at every UE power level.
  Further alignements on simulation assumptions via email (deadline: June, 9th).
Decide in RAN4#84 one of the following options:
    Option 1: 5 us of transient time
    Option 2: 10 usec of transient time
    Option 3: 10 us of transient time and corresponding ON-to-OFF transition step requirements.