## Slide 1: Band plan + EESS/MSS protection levels for TDD L-band
Huawei, Nokia, Etisalat
3GPP TSG-RAN WG4 Meeting #83
Hangzhou, China, 15 - 19 May, 2017
R4-17XXXX

## Slide 2: Way forward 2 TDD Band plans aligned on SDL band plans
1432 MHz |  |  |  |  |  |  |  |  |  |  |  |  |  | 1517 MHz |  | 
1432 - 1437 | 1437 - 1442 | 1442 - 1447 | 1447 - 1452 | 1452 - 1457 | 1457 - 1462 | 1462 - 1467 | 1467 - 1472 | 1472 - 1477 | 1477 - 1482 | 1482 - 1487 | 1487 - 1492 | 1492 - 1497 | 1497 - 1502 | 1502 - 1507 | 1507 - 1512 | 1512 - 1517
TDD 85 MHz (17 blocks of 5 MHz) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1427 MHz | 1432 MHz
1427 - 1432 | 
TDD 5 MHz (1 block of 5 MHz) for Home and LA BS applications only | 

## Slide 3: Way forward MSS protection level
MSS protection at 1518MHz
  1 MHz guard band (1517-1518MHz)
  Protection level for Tx UE => -30dBm/MHz EIRP in the 1518-1559MHz
    No study in the TR, only the MSS protection level -30dBm/MHz EIRP in 1518-1559MHz band
    In the TR, add the A-MPR study and separation frequency study to get the -30dBm/MHz EIRP in 1518-1559MHz band
  Protection level for Tx BTS => Same than SDL

## Slide 4: Way forward EESS protection level
EESS protection at 1427MHz
  Protection level for Tx UE => Same than FDD
    Band 1427-1432MHz (5MHz)
      0 MHz guard band at 1427MHz
      Protection level for Tx UE => -62dBw/27MHz in the 1400-1427MHz => Same than FDD
      In the TR, add the A-MPR (only on 1427-1432MHz band) study as FDD band plan
    Band 1432-1517MHz (85MHz)
      Frequency separation of 5MHz (1427 to 1432MHz)
      Protection level for Tx UE => -62dBw/27MHz in the 1400-1427MHz => Same than FDD
      In the TR, add the A-MPR (only on 1432-1437MHz band) study as FDD band plan
  Protection level for Tx BTS => Same than SDL
    Band 1427-1432MHz (5MHz) => -72dBw/27MHz at the antenna connector in the 1400-1427MHz
    Band 1432-1517MHz (85MHz) => -72dBw/27MHz at the antenna connector in the 1400-1427MHz