## Slide 1: WF on OTA Blocking
CMCC
R4-1706145
Agenda : 10.4.3.1
Document for: Approval
3GPP TSG-RAN WG4 RAN4 #83
Hangzhou, China, May 15th-19th, 2017

## Slide 2: Background
The formula for defining the blocking requirement was set out in last meeting. However, some companies have concerns on the exact parameter values in the formula.
This way forward aims to define the level of the wanted signal and the interference signal. The next slide summarizes three options.

## Slide 3: Way Forward
Option 1:
Wanted signal power = PREFSENS +6dB - 10log(BeWθ.BeWφ) +40.1
Interfering signal power = PConducted interferer– 10log(BeWθ.BeWφ) +40.1
Option 2:
Wanted signal power= Minimum_EIS +6dB
Interfering signal power= PConducted interferer– 10log(BeWθ.BeWφ) +40.1
Minimum_EIS is the declared minimum OTA sensitive in REl13.
OTA REFSENS RoAoA: Is the RoAoA equivalent to the 3 dB beam width of a non-AAS base station passive antenna providing the same coverage as the AAS base station.
BeWθ2 is the beamwidth equivalent to the range of OTA REFSENS RoAoA in the θ-axis in degrees.
BeWφ2 is the beamwidth equivalent to the range of OTA REFSENS RoAoA in the φ-axis in degrees.
Option3:
If the Option 1 is adopted, more information on the OTA performance of the whole AAS system should be given. The required information is FFS.