## Slide 1: WF on new BS requirements
NTT DOCOMO, INC., CMCC
R4-1706158
3GPP TSG-RAN WG4 Meeting #83
Hangzhou, China, 15th – 19th May, 2017
Agenda Item: 10.5.1

## Slide 2: General Background(1/2)
Base on the agreed WF in the last meeting [R4-1704353], NR BS new requirements are discussed in [1-6].
This contribution summarizes way forward/agreement on this topic.
[1] R4-1704541 Proposal on NR BS beam related requirements NTT DOCOMO, INC.
[2] R4-1705236 Proposal on BS specific requirements for NR CMCC
[3] R4-1704920 Consideration on beam related new requirement for NR CATT
[4] R4-1705635 NR Range 2 - beam specific requirements Huawei
[5] R4-1704953 General discussion on expected radiation pattern Ericsson
[6] R4-1704954 Further discussions on radiation patterns: multi-user multi-antenna transmission scheme case Ericsson

## Slide 3: General Background(2/2)
Proposed NR BS new requirements are following. Detail can be found in [1, 2].
In the following slides, background, way forward and agreements on each new requirement are summarised.
No.1 | Guarantee of several fluctuations | [1]
No.2 | Beam steering speed | [1]
No.3 | SLSR and FBR | [2]

## Slide 4: (No.1) Guarantee of several fluctuations
Background
  In [1], it was proposed to clarify in the spec that core requirements are intended to be met over the life of the product.
  Feedbacks that it is applied for the all RAN4 spec without any additional clarification are obtained.
Agreement
  In RAN4-NR#2 meeting (June, 2017), companies encourage to provide the views which is best option.
    Option 1: clarify in the spec that core requirements are intended to be met over the life of the product.
    Option 2: capture the justification in NR WI TR that “additional clarification in the spec is not needed, since it is applied for the all RAN4 spec without any additional clarification”

## Slide 5: (No.2) Beam steering speed
Background
  In [1], it was proposed to introduce Beam steering speed requirement in Rel-15 NR spec, in order to steer the beam direction expeditiously by taking into account UE mobility.
  The aim of requirement is for RF characteristics not for BB or RRM.
Agreement
  The name of “”beam steering speed” should be replaced by “Beam switching speed”
  RAN4 agrees to work to create a description of a RF Beam switching speed requirement for potential introduction in Rel-15 NR core spec is derived based on a for NR BS with analog BF.
    If requirement description becomes agreed, RAN4 introduces the requirement in core spec.
    BB and/or RRM related beam switching speed requirement is FFS.
    Applicability of the requirement is FFS. (e.g., BS power class, Analog or Digital BF etc.)
  In RAN4-NR#2 meeting (June, 2017), companies encourage to provide how to specify RF beam switching speed requirement.
  Feasibility of OTA testing of this requirement should be studied further.
  Even if feasibility is not identified by November, RAN4 would consider whether to introduce the requirement in core spec only (without testing) or not.

## Slide 6: (No.3) SLSR and FBR
Background
  In [2], In order to guarantee the system performance, SLSR and FBR some declarations related to unwanted spatial emissions should be included in the scope of RAN4 specifications for 5G NR BS in Rel-15.
  Since SLSR and FBR spatial emissions are associated with the kind of base station and antenna array, for each base station type and antenna array defines a minimum requirement may be challenging in RAN4.
  For some beamforming algorithms, SLSR and FBR spatial emissions might be traded against in beam wanted EIRP to optimize performance
Agreement
  In RAN4-NR#2 meeting (June, 2017), companies encourage to provide the views which is best option.
    Option1: SLSR and FBR should be included as declarations requirements for 5G NR BS in Rel-15.
    Option2: Side lobe level and front to back ratio potential requirements can be combined into a “emissions spatial mask” declaration
    Option3: Declared The total power that is radiated outside of the 3dB beamwidth within the context of the NR declarations (assuming similar declarations to AAS with this addition)

## Slide 7: Option 1
The declaration for option 1 could look like the following (exact wording to be clarified later)
Unwanted lobe ratio | The ratio of the beam peak EIRP to the largest EIRP that is radiated outside of the 3dB beamwidth. Declared for every beam identified in D9.3.

## Slide 8: Option 2
The declaration for option 2 could look like the following (exact wording to be clarified later)
Unwanted directions set | The set of directions where the AAS BS is intended not to radiated power, declared per EIRP accuracy directions set (D9.8)
Unwanted power level | Maximum power level radiated in the unwanted directions set

## Slide 9: Option 3
The declaration for option 3 could look like the following (exact wording to be clarified later)
Out of beam power | The total power that is radiated outside of the 3dB beamwidth. Declared for every beam identified in D9.3.