## Slide 1: WF on Enhanced CRS-IM Performance Requirements
Intel Corporation, Qualcomm, LGE, CATT
3GPP TSG-RAN WG4 Meeting #83 Hangzhou, China, 15 - 19 May 2017
Agenda Item: 7.27
R4-1706166

## Slide 2: Enhanced CRS-IM for PDCCH/PCFICH (1)
Background:
  Candidate scenarios
  RAN4 #82bis agreements
    Test 3 (4 RX antennas + 4 CRS APs)
      Provide additional analysis in RAN4 #83 for Medium correlation channel model
      Decide on performance requirements introduction in RAN4 #83
        Option 1: Do not define requirements
        Option 2: Define demodulation requirements for Medium antenna correlation model based on Type A CCIM receiver
        Option 3: Define demodulation requirements for Medium antenna correlation model based on LMMSE-IRC receiver
        Option 4: Define demodulation requirements for Low antenna correlation model based on LMMSE-IRC receiver (without CRS-IM)
Test | CRS pattern | Number of UE RX chains | Number of CRS APs | 
 |  |  | Serv. cell | Interf. cell
1 | Non Colliding | 2 | 4 | 4
3 | Non Colliding | 4 | 4 | 4

## Slide 3: Enhanced CRS-IM for PDCCH/PCFICH (2)
Test 3 (4 RX antennas + 4 CRS APs)
  Define demodulation requirements
    Low antenna correlation model
    PDCCH AL1
    Requirements are based on LMMSE-IRC receiver (without CRS-IM)

## Slide 4: UE Feature List
Background: RAN4 82bis agreements
  Set of UE features
    #1: Non-colliding CRS-IM receiver for 2RX and 4 CRS APs for PDSCH
    #2: Non-colliding CRS-IM receiver for 4RX and 2 CRS APs for PDSCH
    #3: Non-colliding CRS-IM receiver for 4RX and 4 CRS APs for PDSCH
    #4: Type A CCIM receiver for 2RX and 4 CRS APs for DL Control Channels
    FFS depending on the test case introduction
      #5: Type A CCIM receiver for 4RX and 2 CRS APs for DL Control Channels
      #6: Type A CCIM receiver for 4RX and 4 CRS APs for DL Control Channels
    FFS depending on the capability signalling discussion
      #7: Blind detection of base CRS assistance information including number of CRS-APs
RAN4 83 agreements
  Introduce additional UE features
    #5: Type A DL Control Channels IM receiver for 4RX UEs
  FFS depending on the capability signalling discussion
    #6: Blind detection of base CRS assistance information including number of CRS-APs