## Slide 1: Way forward on SI acquisition time requirements for non-BL/CE UE
Ericsson
3GPP TSG-RAN WG4 Meeting #83
Hangzhou, 15 - 19, May, 2017
R4-1706183

## Slide 2: Background
It is observed MIB acquisition time and SIB1-BR acquisition time for 2Rx UE with SNR=-15dB are improved significantly compared with 1Rx UE.
Source | Tdoc number | MIB acquisition time (99% PBCH decoding success rate with SNR=-15dB) |  | SIB1-BR acquisition time (99% PDSCH decoding success rate with SNR=-15dB) (Repetition = 16) | 
 |  | EPA1 | ETU1 | EPA1 | ETU1
Intel | R4-1704707 | 17 TTI | 14 TTI | 3 TTI | 5 TTI
Nokia | R4-1705728 | 13 TTI | 17 TTI | 6 TTI | 4 TTI
Ericsson | R4-1704814 | 13 TTI | 14 TTI | 8 TTU | 10 TTI
Note 1: TTI=40ms for MIB acquisition time
Note 2: TTI=80ms for SIB1-BR acquisition time

## Slide 3: Way forward
RAN4 will consider shortening the SI acquisition time testing requirement for non-BL CE Mode B UE assuming 2Rx in Rel-14.
RAN4 will consider how to clarify the SI acquisition time requirement for non-BL CE Mode B UE assuming 2Rx in Rel-14 in the core requirement.
Companies are encouraged to propose the SI acquisition time for non-BL CE Mode B UE based on the practical simulation results in RAN4#84.

## Slide 4: Simulation assumption
Parameters | CE Mode B
System bandwidth | 10MHz
Transmit antennas | 2
Propagation channel | EPA1, ETU1
TBS for SIB1-BR | 152 bits
SIB1-BR repetition number | 16
PBCH repetition | Enabled
UE receive antenna | 2
UE frequency offset | 100 Hz
Evaluation criteria | 99% MIB decoding success rate at SNR=-15dB 99% SIB1-BR decoding success rate at SNR=-15dB