## Slide 1: Way forward on non-BL/CE UE RLM evaluation period
Ericsson
3GPP TSG-RAN WG4 Meeting #83
Hangzhou, 15 - 19, May, 2017
R4-1706184

## Slide 2: Background
Rel-13 RLM measurement period for BL/CE UE, when no DRX is used, is specified as follows:
It is observed MPDCCH demodulation performance with 2Rx UE is about 2-3dB better than 1Rx UE considering 2%/10% BLER.
 | Out-of-synch | In-sync
CE Mode A | 400ms | 200ms
CE Mode B | 4000ms | 2000ms

## Slide 3: Way forward
RAN4 will study the RLM evaluation period for BL/CE UE with 2Rx, when no DRX is used, for the following scenarios in Rel-14
  CE Mode A Out-of-synch
  CE Mode A In-synch
  CE Mode B Out-of-synch
  CE Mode B In-synch
Companies are encouraged to provide the investigation results for the RLM evaluation period considering the effectiveness of receiver diversity in RAN4#84
  Side condition:
    CE Mode A: EPA5/ETU30 with SNR = -6dB
    CE Mode B: EPA1/ETU1 with SNR = -15dB