## Slide 1: WF on requirements for Rel-13 Non-BL UE
Huawei, HiSilicon, Ericsson, Intel Corporation, Qualcomm
R4-1706196
3GPP TSG-RAN4 Meeting #83
Hangzhou, China, 15th – 19th May 2017

## Slide 2: Background
The Rel-13 Coverage Enhancement (CE) feature can be supported by any LTE UE category and not restricted to be used for Category M1 devices (i.e., BL/CE UEs) only.
Existing UE demodulation performance and CQI requirements for the CE feature are defined based on the simulation results with the Category M1 devices with single receive antenna
  It is not clear how to setup the test for demodulation and CQI requirements for devices with 2 and 4 receive antennas supporting CE
  The requirements for the devices with 2 and 4 receive antennas are not defined and existing Cat-M1 requirements may not be directly reused
  Existing UE demodulation performance and CQI requirements for the CE feature are defined based on the simulation results with the Category M1 devices with single receive antenna

## Slide 3: Background
  Achieved agreements
    Existing Rel-13 CE UE demodulation requirements are applicable for “UE Category 1 + 1RX”.(WF, R4-1702164)
    Apply Rel-13 CE UE demod & CQI requirements to DL Category 0 without any modifications.(Chairman note, R4-1704501)
    4 options were proposed in RAN4# 82bis which needs down selection. (WF, R4-1704178 )(show in page 4).

## Slide 4: Background
 | Antenna connection | Test setup and parameters | Requirements
Option 1-1 | Simplified antennas connection method (See appendix). The existing CE tests are performed by duplicating the fading channel from each Tx antenna and adding independent noise for each Rx antenna. | Same as Rel-13 eMTC except reduced SNR for CQI definition test | Same as Rel-13 eMTC.
Option 1-2 | Simplified antennas connection method (See appendix). The existing CE tests are performed by duplicating the fading channel from each Tx antenna and adding independent noise for each Rx antenna. | Same as Rel-13 eMTC except reduced SNR for CQI definition test | Add some margins to the Rel-13 requirements depending on the number of receive antennas
Option 2 | Full antenna connection method. New CE tests with full channel models are defined under assumption that channel fading is independently generated for each RX antenna. | Reuse the Rel-13 eMTC setting. Repetition number may be adjusted. | New requirements
Option 3 | Connect one antenna port regardless of the number of receive antennas. Rest of antenna ports are open or terminated. | Same as Rel-13 eMTC. | Same as Rel-13 eMTC.

## Slide 5: Agreements
Define new UE demodulation and CQI requirements for non-BL UE supporting coverage enhancements with 2Rx/4Rx using full antenna connection (i.e., Option 2) from Rel-13.
  UE demodulation requirements
    Reuse setup for category M1 (except repetition numbers) specified for Rel-13 Cat-M1 UE requirements.
    Repetition numbers would be adjusted to meet considering the target SNR for CE Mode A (-6dB) and CE mode B (-15dB).
      Option 1:Adopt a half and a quarter of repetition number for category M1 to define requirements for others categories with 2 Rx and 4Rx respectively.
      others options are not precluded.
  CQI tests
    Reduce of SNR test points

## Slide 6: UE demodulation requirements
Interested companies are encouraged to submit the ideal simulation results with 2Rx/4Rx for the test cases below in RAN4#84.
  Companies are also encouraged to propose the repetition numbers to keep the same target SNR levels as the existing Cat-M1 test cases except for non repetition test cases.
Test cases | Reference in TS36.101
MPDCCH CE Mode A | 8.11.2.1.1 / 8.11.2.2.1
MPDCCH CE Mode B | 8.11.2.1.2 / 8.11.2.2.2
PDSCH TM6 | 8.11.1.1.1 / 8.11.1.2.1
PDSCH TM9 | 8.11.1.1.2 / 8.11.1.2.2
PDSCH TM2 | 8.11.1.1.3 / 8.11.1.2.3

## Slide 7: CQI tests
Interested companies are encouraged to propose the test points for the following CQI tests for non-BL UE with 2Rx/4Rx in RAN4#84, e.g., 3dB for 2Rx and 6dB for 4Rx.
  CQI definition tests specified in TS36.101 9.8.1
  UE-selected subband CQI tests specified in TS36.101 9.8.2

## Slide 8: Rel-14 test cases
FFS for applicability of Rel-14 Cat-M2 test cases
FFS for Rel-14 non-BL UE requirements supporting 96PRB.