## Slide 1: Summary of discussions on UE capabilities signalling related to MIMO layer
Ericsson
3GPP TSG-RAN WG4 Meeting #83 R4-1706201 Hangzhou, China, 15th-19th May, 2017
Document Type: For information

## Slide 2: Background
RAN4 received an LS from RAN2 in R2-1702346 asking TM10/FD-MIMO capability related parameters are RF or BB capability.
RAN4 is preparing the LS on MUST to decide the UE capability for MUST in R4-1704642.
RAN4 is preparing the RAN4-led WI feature lists in R4-1705658

## Slide 3: Observation
For baseband feature capabilities such as NAICS, CSI-processing, etc., as long as it’s considered as sharing baseband processing capability together with MIMO layer, even if they are baseband capabilities they are reported in the same way as MIMO layer as per band combination manner.
There are inconsistency of the existing baseband capabilities design, e.g. some capability such as hybridCSI-r14, semiOL-r14 are not linked with MIMO layer reported as per UE and some capability such as number of CSI-process, csi-ReportingNP-r14, csi-ReportingAdvanced-r14 are linked with MIMO layer reported as per band combination.

## Slide 4: Common understanding
From RAN4 point of view it should be feasible to
  Split the existing supported MIMO layer capability into RF band part and baseband part capability separately.
  Report the supported MIMO layer RF capability as a maximum supported MIMO layer per band.
  Report the baseband features in a combined way with all related supported baseband features including CA (CA bandwidth combination and number of CCs) and MIMO layer baseband capability etc. as per UE.

## Slide 5: Consideration for BB capability
All baseband features listed as following should be considered as sharing the same baseband processing resource pool so the baseband capability design should be considered in an joint manner.
  MIMO layer, NAICS, MUST, number of CSI-processing, FD-MIMO, TM10, 4Rx, 256QAM, advanced receivers such as CRS-IC, MMSE-IRC, R-ML, etc.
The above baseband features should be considered together with the number of CCs and the aggregated bandwidths from CA.
Different combinations of supporting different baseband features together with the number of CCs and aggregated bandwidths should be allowed.
The exact signaling design on how to report the joint baseband capability per UE should be up to RAN2 to decide.
Similar methodology of reporting baseband capability could be taken as a good reference for NR in case we could reach agreement for LTE.

## Slide 6: Way forward
Interested companies check the possibility on how to capture the common understanding from RAN4 and further consider what could be considered as practical solution for the baseband capability reporting.
In next meeting the goal is to come up with a conclusion for the improvement of the signaling in LTE timeframe.