## Slide 1: Way forward on eMTC subband CQI test
Ericsson, Anritsu, Qualcomm
3GPP TSG-RAN WG4 Meeting #83
Hangzhou, 15 - 19, May, 2017
R4-1706204

## Slide 2: Background
The current test spec for the sub-band CQI test for eMTC in TS36.101 9.8.2.1 specifies MPDCCH narrowband = 7, MPDCCH repetition (Rmax) = 1 and hopping interval = 8.
With the setting, according to TS36.211, UE can monitor narrowband #7 only, but cannot monitor other narrowbands (#0, #1, #2).
This setting cannot verify the UE preferred narrowband from 4 narrowbands.
Reference: R4-1704768

## Slide 3: Way forward
Companies are encouraged to evaluate the setting below and provide the simulation results for subband CQI test (i.e., gamma) in RAN4#84.
  UE should monitor 4 narrowbands (#7, #0, #1, #2) with the same probability.
  MPDCCH narrowband = 7 (mpdcch-Narrowband)
  MPDCCH repetition = 4 (mpdcch-NumRepetition)
  G = 2.5 (mpdcch-StartSF-UESS)
  Hopping interval = 1 (interval-FDD)
Other setting is not precluded if any issues are found.