## Slide 1: WF on demodulation performance for V2X UE
3GPP TSG-RAN WG4 Meeting #83 Hangzhou, China, 15 - 19 May, 2017
Agenda Item: 7.16.5
R4-1706213
CATT, LG Electronics, Huawei

## Slide 2: Background
In RAN4#82bis meeting, the following agreements were reached:
  Introduce new test case for PSBCH performance requirement
  Introduce new test case for PSSCH decoding capability requirement
  Introduce new test cases for PSCCH decoding capabilities (X=10 and X=20) requirements
  Need to investigate PSCCH/PSSCH performance based on eNB synchronization source
  Need further analysis and test methodology on WAN SDR test activated V2X communication
  Work plan (R4-166984) to finish performance part on time (~ September, 2017)
  RAN4 # 84
    Approve CRs on V2X demodulation test cases
    Complete demodulation performance requirement
  Companies are encouraged to provide alignment and impairment results for identified test cases for V2X UE

## Slide 3: PSBCH test
Simulation assumption
  Timing and Frequency offset in Rx side
    24 Ts and 600Hz as baseline
CFO estimation algorithm
  leave to UE implementation
Test metric
  SNR@1% PSBCH BLER

## Slide 4: PSSCH decoding processing test
Test metric
  SNR @ 10% PSSCH BLER

## Slide 5: PSCCH decoding processing test
Test configuration
  For Type 1: X=10, Y=100
  For Type 2: X=20, Y=136
    Do not consider PSSCH overlapping test configuration
    Focus on verifying X as baseline
Test metric
  Companies are encouraged to provide analyses in next meeting.

## Slide 6: eNB synchronization source based test
Definition for performance requirement
  Define 1 new test case for PSSCH
  Frequency offset
    V2X UE derives synchronization from other eNB than serving cell, taking into account of inter cell synchronization error.

## Slide 7: WAN SDR test activated V2X communication
Definition for performance requirement
  Combining legacy WAN SDR test and V2X PSSCH decoding processing test to verify the concurrent WAN and V2X communication operation, the test purpose is:
    The WAN reception in not impacted when PC5-based V2X is concurrent with WAN operation and the PC5-based V2X reception is not impacted by WAN reception either.
  Further study applicability rules and companies can further check the feasibility of the test.

## Slide 8: Other issue
Power imbalance test
  RAN4 agree ICS level is [-25] dBc for power imbalance test
  If technical issues are observed with -25dBc ICS level to support V2X, ICS level could be revised