## Slide 1
3GPP TSG-RAN WG4 RAN4 #83
Hangzhou, China, May 25th-19th, 2017
R4-1706222
WF on NR BS mmWave unwanted emission
Nokia, Alcatel-Lucent Shanghai Bell

## Slide 2: Way forward on NR BS mmW spectrum emission mask
NR BS mmW spectrum emission mask should be defined taking into account following assumptions:
  NR should have the boundary between OOB and spurious domain limits defined by regulation
  Masks in the Out-of-band domain should be carrier frequency centric SEM
  The NR emission mask (SEM) should use the emission limits submitted to WP5D as a baseline
    Further investigations of SEM limits for different channel bandwidths, BS power levels and BS classes to be conducted
  Investigate possibility to specify multiple fixed boundaries according to carrier channel bandwidth and/or frequency range for unwanted emissions
  Agreed ACLR values should be considered

## Slide 3: Way forward on NR BS mmW spurious emission
Upper boundary of fundamental frequency range for BS spurious emission should be specified to cover at least 28GHz NR bands
  i.e. Upper limit of frequency range should be 56GHz as a 2nd harmonic.
OTA testability for high frequency should be further studied and taken into account for higher frequency bands
Investigate how to specify OTA requirements together with EMC, since emissions from antenna and enclosure cannot be separated