## Slide 1: WF on BS spectrum emission mask for below 6GHz
ZTE,Huawei,Nokia,Ericsson,[NTT DoCoMo,…]
3GPP TSG-RAN WG4 Meeting #83 Hangzhou, China, 15 - 19 May, 2017
Agenda Item: 10.5.3.2
R4-1706223

## Slide 2: Background
Contributions on BS spectrum emission mask for below 6GHz have been discussed in RAN4#83:
R4-1704542,Proposal on below 6GHz NR BS unwanted emission mask requirement, NTT DoCoMo
R4-1704616, NR BS boundary between out-of-band and spurious domain below 6 Ghz,Ericsson
R4-1705268,The boundary between out-of-band and spurious domain below 6 GHz NR BS,ZTE
R4-1705285,BS spectrum emission mask for below 6GHz,Huawei, Hisilicon
Clarification:
In the current TS36.104, for the band42 from 3.4GHz to 3.6GHz with ΔfUEM =10 MHz specified, at that phase RF requirement didn’t take the large antenna arrays into account, however for NR bands, wider operating bandwidth and large antenna arrays should be considered.

## Slide 3: Way forward on spectral emission mask
ΔfUEM =40 MHz for NR bands wider than 100 MHz as baseline for the boundary between UEM and spurious emission( for both Cat A and Cat B );
The same emission levels for LTE should be used with frequency range (FDL_low– ΔfUEM) ~ (FDL_high+ΔfUEM)
Applicability of regional requirement for NR only bands could be considered further, however relaxed regional emission mask should be excluded for further discussion;