## Slide 1: WF on Multi-node tests
Qualcomm, Ericsson, Huawei, HiSilicon, Nokia, Alcatel-Lucent, Shanghai Bell, Verizon, AT&T, US Cellular, Vodafone, Orange, Skyworks, Samsung, T-Mobile USA, MediaTek, Broadcom, Blackberry, CableLabs, Brocade, Blackberry
3GPP TSG-RAN WG4 #83
May 15th – 19th, 2017
Hangzhou, China
R4-1706224

## Slide 2: Agreements from RAN4 #82bis: Purpose and goal of TR 36.789
Based on the Multi-node study, the outcome of Multi-node test SI should be an evaluation methodology which allows to assess the impact for both LAA to other systems, e.g. Wi-Fi and other systems e.g. Wi-Fi to LAA
The evaluation methodology needs to provide the necessary tools to run the coexistence tests, including:
  Test setup, e.g. number of nodes
  Signal levels and SIR operating points
  Evaluation metrics
  …
The scope of TR 36.789 is not to mandate a specific implementation

## Slide 3: Agreements in RAN4 #83 (1)
General agreements:
  RAN4 tests in TR 36.789 provides an overall evaluation methodology rather than a specific pass/fail criteria
    This document aims to provide an evaluation methodology for multi-node coexistence between Rel-13 LAA BSs and other wireless systems.
Receiver signal levels and SIR:
  Configuration with low RSSI and low SIR to be listed in the TR
  All the configurations below are recommended for testing. Which configuration(s) is(are) to be tested and how to interpret the significance is based on specific deployment scenario.
Device selection criteria
  Wi-Fi alliance certified devices
Intefering Links between DL nodes | Wanted Signal Links |  | Interfering Links between DL and UL nodes |  | 
Link A-B | Link A-C | Link B-D | Link A-D | Link B-C | Note
-67dBm/20MHz | -57dBm/20MHz | -57dBm/20MHz | -67dBm/20MHz | -67dBm/20MHz | SIR = 10dB
-67dBm/20MHz | -67dBm/20MHz | -67dBm/20MHz | -67dBm/20MHz | -67dBm/20MHz | SIR = 0dB
-80dBm/20MHz | -70dBm/20MHz | -70dBm/20MHz | -80dBm/20MHz | -80dBm/20MHz | SIR = 10dB
-80dBm/20MHz | -80dBm/20MHz | -80dBm/20MHz | -80dBm/20MHz | -80dBm/20MHz | SIR = 0dB

## Slide 4: Agreements in RAN4 #83 (2)
Traffic type selection:
  mixed traffic type in aggressor link is considered
Details about evaluation criteria:
  Normalized throughput is considered as a metric for the throughput tests
  A CDF curve of the performance metric is part of the evaluation criteria
  50% is the most relevant point for performance comparison. Other points, e.g. 25% and 75% could be considered

## Slide 5: Open items to be agreed by email discussion
The following open items should be agreed by email discussions:
  For the metric of the outage test one of the following metrics should be selected:
    Option 1: Delay and Jitter
    Option 2: MOS score with the precise MOS function to be provided
  It should be decided whether to disable discontinuous transmissions on the Wi-Fi AP or LAA BS (such as LAA DRX, 802.11 Power Save, background scanning etc.) and whether devices shall run the most recent vendor-supplied firmware
  The minimum number of devices which should be used to define the baseline (e.g. [10] APs and [10] STAs to create the Wi-Fi to Wi-Fi baseline)
Email discussion needs to be finalized by 05/26/2017
The outcome of the email discussion agreements should be capture in the TP to TR 36.789 submitted to RAN #76