## Slide 1: WF on eMTC BS PRACH requirements
Nokia, Alcatel-Lucent Shanghai Bell, Huawei…
3GPP TSG-RAN WG4 Meeting #83
Hangzhou, China, May 15 – 19, 2017
R4-1706263

## Slide 2: Background
The eMTC PRACH performance are defined for frequency hopping ON case, but hopping related parameters are not specified, which make it difficult for BS and TE to have common understanding about the PRB locations of PRACH transmissions during the test.
The eMTC PRACH performance are defined as a single set of requirements applicable for all system BWs from 3MHz to 20MHz. However, the diversity gain due to hopping is dependent on the system BWs.

## Slide 3: WF
Define frequency hopping related parameters in eMTC PRACH performance test case in 36.104 and 36.141
  PRACH frequency offset (prach-FreqOffset-r13) is 0
  PRACH frequency hopping offset (prach-HoppingOffset-r13) is N_RB^UL - 6, where N_RB^UL is the UL bandwidth configuration as defined in TS36.211
Interested companies are encouraged to evaluate the PRACH performance with frequency hopping for all system BWs from 3MHz to 20MHz based on TS36.104 Table 8.4.2.1-4. RAN4 will down-select the solution on how to update the performance requirements from the following options
  Option 1: Define separate requirements for each system BW
  Option 2: Relax the current requirement by [X]dB and apply this requirement to system BW from 5MHz to 20MHz. Apply the requirement without frequency hopping for 3MHz.
RAN4 should agree on the solution for PRACH performance requirements and finalize the CR in RAN4#84.