## Slide 1: WF on Channel Bandwidth
Qualcomm Incorporated
3GPP TSG-RAN WG4 RAN4 #83
Hangzhou, China, May 25th-19th, 2017
R4-1706321
Agenda : 10.3.1
Document for: Approval

## Slide 2: Background for Support of New Channel Bandwidths
Addition of new maximum channel bandwidths in a backwards compatible way should be allowed in a future release
  Legacy UEs should still be able to operate in a channel with the newly introduced bandwidth
  The gNB may configure a new CHBW that is not supported by legacy UEs but these UEs can still operate in this channel
  Handling of the gNB configured CHBW with CA by the UE that does not support this CHBW needs to be supported in the specifications for forward compatibility
    RAN1 already agreed this [R1-1706615]
  gNBs will have to handle UEs that support the largest gNB configurable CHBW with CA such that legacy UEs can operate their entire aggregated bandwidth despite having limited CHBW
  All CHBW to be supported by UE shall be defined in the spec
    Support of which CHBW is mandatory is FFS
MaxCHBW 400MHz
CHBW 200MHz
MaxCHBW400MHz
CHBW
200MHz
MaxCHBW 600MHz
MaxCHBW 600MHz
Rel.15
Future Release
Addition of
600MHz CHBW
gNB
Rel-15 UE
UE supported bandwidth in band
RFBW = 600MHz
MaxCHBW400MHz
CHBW
200MHz
UE supported bandwidth in band
RFBW = 600MHz
Rel-16 UE
UE supported bandwidth in band
NOTE: UE cannot operate a wider CHBW than BS is operating

## Slide 3: Agreements from RAN4 #83

## Slide 4: Agreements
Addition of new maximum channel bandwidths is allowed in future releases
  NR design should ensure forward compatibility, send LS to RAN1/2 to inform about this agreement
  Addition of new UE channel bandwdiths that are not larger than previously defined maximum in the band is FFS.
UE is allowed to aggregate channel bandwidths to operate within a gNB configurable CHBW that is higher than the maximum bandwidth supported by the UE
  For example, a 400MHz UE that does not support 400MHz channel bandwidth can support 2x200MHz or 4x100MHz even if the gNB could configure 400MHz channel bandwidth
    Each CC bandwidth is from the set of channel bandwidths defined for that band
  UE should indicate to gNB its bandwidth capability and how it supports this bandwidth (e.g. what CA combination)
    Signaling details are FFS
  Which aggregated channel bandwidth combinations are allowed is FFS, BS complexity should be considered

## Slide 5: Agreements
All defined channel bandwidths should be supportable by at least one type of UE capability
UE shall support any Rel-15 channel bandwidth that is smaller than its UE supported maximum channel bandwidth.
The set of channel bandwidths specified in Rel-15 shall be band and SCS specific.
  A definition for channel bandwidth is required in the BS spec, for testing certain requirements, such as ACLR & ACS. However the exact definition and how it relates to Base Station RF Bandwidth is FFS.
  the actual BS RF bandwidth can be different from the channel bandwidth (as shown in the figure on slide 2).
  Implementation and support of channel bandwidths in the specs will be done in order to minimize market fragmentation of UE.
The maximum channel bandwidth supported by UE can be different for UL & DL and SCS specific.
Base station RF bandwidth can be larger than the largest channel bandwidth specified in Rel-15.

## Slide 6: Maximum channel bandwidth (CHBW) in Rel. 15
For bands below 6GHz
  100MHz maximum CHBW
For bands above 24GHz
  400MHz maximum CHBW
Different maximum channel bandwidths can defined for different SCS
  Maximum channel bandwidths for certain SCS can be smaller than the ones listed above but not larger
Not all UEs need to support the maximum channel bandwidth but the maximum channel bandwidth specified in UE specs shall not be lower than the maximum channel bandwidth specified in BS specs