## Slide 1: Way Forward on mmW power class
Qualcomm, Ericsson, Sony
3GPP TSG-RAN WG4#83 R4-170xxxx
Hangzhou, CHINA, 15 - 19 May, 2017
Agenda: 10.4

## Slide 2: Background
mmW UE power class definition has been discussed in many meetings
In RAN4#82Bis, WF [1] was agreed with the text:
  UE must be able to produce certain EIRP
  Powerclass definition includes upper limit for TRP which need to be met regardless of beamforming settings
  Further details for power class definition are FFS
In RAN4#82, it was agreed that
  Agreement:
  Proposal: For CDF method, RAN4 method for describing spherical coverage of RF parameters is CDF where each point represent equal surface area in sphere surrounding the UE.
    Companies are encouraged to study the advantage of this CDF method.
    The other method(s) are not precluded.

## Slide 3: Background
In this meeting, several papers discussed and proposed how to apply the agreement to power class definition
For minimum EIRP
  Peak / boresight EIRP was proposed in [3], [6]
  Min EIRP requirement for 50 % CDF (50 % of the beams) was proposed in [4] and [5] and was outline as one possibility in [3]
  Min EIRP of 20, 50, 80 % tile was proposed in [10]
For maximum EIRP
  Max 43 dBm EIRP was proposed in [8]
  30 dBm in [9]
For TRP
  Max 23 dBm was proposed in [5]
  Nominal TRP values for 28 GHz were discussed in [11]
  Maximum TRP with value as FFS was proposed in [2], [3], [4], [8] and [9]

## Slide 4: Background
Issues discussed in this meeting for applicability of power class definition in relation to
  Definition of Unwanted emissions (ACLR, SEM, Spurious Emissions)
  Reference power in Power control related aspects (TS 38.213)
  Constraints on UE Antenna design
  Co-channel interference
  UL Link budget
  Multibeam UEs
  Co-existence study assumptions (23 dBm conducted power, 20 dBm per polarization, with 4 antenna elements and 5 dBi element gain)
  UE spherical coverage requirements
  MPR and A-MPR definitions

## Slide 5: Way Forward on mmW UE power class
Both TRP and EIRP are considered for power class definition
  EIRP can be peak, boresight or %-tile or minimum value
  TRP can be max or min and max
Max allowed EIRP for all UEs is 43 dBm for regulatory reasons
Companies are encouraged to provide input
  For discussed issues mentioned in previous slides and their relevance for power class definition
  Feasible UE output power values, both TRP and EIRP considering different implementations
  Understanding of co-existence study outcome and impact to power class definition
  Feasible definition and values for spherical coverage
Definition and values for power class and other in channel output power requirements will be decided in RAN4-NR#2 in Qingdao based on input

## Slide 6: References
[1] R4-1704362, “WF on mmWave powe class” Qualcomm, Ericsson, Sony, Skyworks
[2] R4-1704531, “NR – UE Power Class definition for cmW and mmW ranges”, InterDigital, Inc.
[3] R4-1705201, “Output power Requirement for mmW”, Qualcomm
[4] R4-1705222, “Further discussion on mmWave power class definition”, Huawei, HiSilicon
[5] R4-1705226, “mmWave UE power class definition”, Sumitomo Elec. Industries, Ltd
[6] R4-1705677, “mmW UE power class”, MediaTek Inc.
[7] R4-1704686, “On consideration of mmWave UE power class”, Intel Corporation
[8] R4-1705106, “Definition of UE power class”, Ericsson, Sony
[9] R4-1704934, “Transmitter RF requirements for NR UE”, LG Electronics Inc.
[10] R4-1705223, “Further discussion on mmWave EIRP/EIS requirement following CDF approach”, Huawei, HiSilicon
[11] R4-1705107, “UE power classes for 28 GHz”, Ericsson, Sony