## Slide 1
3GPP TSG-RAN WG4 #84 R4-1707432 Berlin, Germany, 21 - 25 August, 2017
Agenda item: 7.16.1 - RF [TEI14]
Document for: Approval
On clarifying applicability of NOTE in TS36.101
KDDI Corporation

## Slide 2: Background
CA_1A-41A (and CA_1A-41C as well) was standardized with restriction that B41 UL transmission was not allowed.
This restriction was captured in several tables of TS36.101.
However, one of notes in TS36.101 includes ambiguity. There is possibility to cause misunderstanding.
We would like to correct this situation but at first, feedback from RAN4 experts would be appreciated.

## Slide 3: Problematic point
E-UTRA CA configuration / Bandwidth combination set |  |  |  |  |  |  |  |  |  | 
E-UTRA CA Configuration | Uplink CA configurations (NOTE 4) | E-UTRA Bands | 1.4 MHz | 3 MHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | Maximum aggregated bandwidth [MHz] | Bandwidth combination set
… (Non-related parts Omitted)… |  |  |  |  |  |  |  |  |  | 
CA_1A-41A8 | - | 1 |  |  | Yes | Yes | Yes | Yes | 40 | 0
 |  | 41 |  |  | Yes | Yes | Yes | Yes |  | 
(Non-related parts Omitted) |  |  |  |  |  |  |  |  |  | 
NOTE 1: The CA Configuration refers to a combination of an operating band and a CA bandwidth class specified in Table 5 ・・・（Non-related parts Omitted）・・・ NOTE 8: For the corresponding CA configuration, UE may not support Pcell transmissions in this E-UTRA band |  |  |  |  |  |  |  |  |  | 
Table 5.6A.1-2: E-UTRA CA configurations and bandwidth combination sets defined for inter-band CA (two bands)

## Slide 4: 2 types of interpretation
CA_1A-41A 8
#1
NOTE8 applies to “CA_1A-41A”. (This is NOT correct interpretation)
CA_1A-41A 8
#2
NOTE8 applies to only “41A”. (This is correct)
NOTE 8: For the corresponding CA configuration, UE may not support Pcell transmissions in this E-UTRA band.

## Slide 5: Consideration
If CA combination like below exists in TS36.101, everyone has common understanding that NOTE8 applies only single band not CA configuration.
However, unfortunately, there is no CA combination, which has NOTE8 on left side band so far.
CA_xA 8-yA

## Slide 6: Proposal
We propose to modify NOTE8 in Table 5.6A.1-2 of TS36.101 as following;
E-UTRA CA configuration / Bandwidth combination set |  |  |  |  |  |  |  |  |  | 
E-UTRA CA Configuration | Uplink CA configurations (NOTE 4) | E-UTRA Bands | 1.4 MHz | 3 MHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | Maximum aggregated bandwidth [MHz] | Bandwidth combination set
… (Non-related parts Omitted)… |  |  |  |  |  |  |  |  |  | 
CA_1A-41A8 | - | 1 |  |  | Yes | Yes | Yes | Yes | 40 | 0
 |  | 41 |  |  | Yes | Yes | Yes | Yes |  | 
(Non-related parts Omitted) |  |  |  |  |  |  |  |  |  | 
NOTE 1: The CA Configuration refers to a combination of an operating band and a CA bandwidth class specified in Table 5 ・・・（Non-related parts Omitted）・・・ NOTE 8: For the corresponding CA configuration, UE may not support Pcell transmissions in this E-UTRA band 41. |  |  |  |  |  |  |  |  |  | 
Table 5.6A.1-2: E-UTRA CA configurations and bandwidth combination sets defined for inter-band CA (two bands)

## Slide 7: Conclusion
In order to have universal understanding, we propose to modify NOTE8 in Table 5.6A.1-2 of TS36.101.
When RAN4 can approve this, tdoc numbers for CRs will be requested.
NOTE 8: For the corresponding CA configuration, UE may not support Pcell transmissions in this E-UTRA band
NOTE 8: For the corresponding CA configuration, UE may not support Pcell transmissions in this E-UTRA band 41.
before
after

## Slide 8: Others
In current version of this specification, NOTE8 in Table 5.6A.1-2 applies below CA combinations.
  CA_1A-41A
  CA_1A-41C
  CA_25A-41A
  CA_25A-41C
  CA_25A-41D