## Slide 1: MIMO OTA TRMS requirements for B41 and B38
CATR, CMCC, OPPO, Xiaomi
3GPP TSG-RAN WG4 Meeting #84 R4-1707752
Berlin, Germany, 21-25 August, 2017
Agenda item: 7.2.1.2
Document for: Approval

## Slide 2: Background
The MIMO OTA requirements framework was approved during the last MIMO OTA Ad-hoc [R4-1706413];
TRMS results for band 41 have been provided and discussed [R4-1706405, R4-1707754];
The analysis of TRMS performance for B41 and B38 were discussed [R4-1707755];
This is the last meeting in MIMO WI extension, the aim is to finalize the requirements for PS1;
Based on the discussion in [R4-1707754] [R4-1707755], the TRMS requirements for B41 and B38 can be agreed in this meeting.

## Slide 3: B41 and B38 requirements
Values in table below should be approved as MIMO OTA TRMS requirements for B41 and B38 in free space configuration:
Channel Model |  | SCME urban micro-cell | 
Operating band | RS-EPRE Unit | TRMS | 
 |  | Average, 70 | Average, 95
41 | dBm/15 kHz | -96 | -94
38 | dBm/15 kHz | -96 | -94