## Slide 1: WF on 1 RX CRS-IM performance
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #84 Berlin, Germany, 21 - 25 August 2017
Agenda Item: 8.31
R4-1708681

## Slide 2: Introduction
In RAN #76 meeting a new RAN4 WI “LTE CRS-IM Performance Requirements for Single RX Chain UEs” (1RX CRS-IM WI) was approved and has the following objectives:
  Phase I:
    Investigate the general impact of CRS-IM on power consumption, complexity and throughput gain for the UEs equipped with 1Rx chain
    Investigate the feasibility of CRS-IM receivers for the UEs equipped with 1 RX chain
      Identify target scenarios including deployment scenarios, interference models, and others.
        Reuse Rel-13/14 CRS-IM assumptions as the starting point.
      Identify reference CRS-IM receiver structure assumptions including at least number of cancelled interference cell(s)
      Evaluate the CRS-IM performance benefits for the Single RX chain UEs
  Phase II:
    After completion of Phase I, specify UE demodulation and CSI reporting performance requirements for the UEs equipped with 1 RX chain

## Slide 3: Target device types / UE categories
Investigate 1RX CRS-IM feasibility and specify requirements for the following UE types:
  1st priority: Cat1bis (UE Cat 1 with 1 RX), CatM2
  2nd priority: Other 1RX device categories (e.g. CatM1)

## Slide 4: Scenarios and assumptions
Physical channels
  Investigate 1RX CRS-IM feasibility for the following physical channels:
Physical channels | UE categories | 
 | Cat1bis | CatM2 (CatM1)
PDSCH (1st priority) | PDSCH TM4 and TM9 can be considered similar to the Rel-14 CRS-IM requirements. FRCs: Rank 1 + QPSK 1/3; Rank 1 + 16QAM 1/2; Rank 1 + 64QAM ½ | TM6 can be considered at the initial stage. FFS if TM9 and TM2 requirements are needed. FRCs: QPSK 1/3; 16QAM 1/2 Focus on CE mode A Single repetition level as the starting point. Reuse TS 36.101 test case 8.11.1.1.1.1 as the starting point
DL control channels (2nd priority) | PDCCH AL 2, 4, 8 CFI = 1 or 2 | Focus on CE mode A Single repetition level as the starting point.

## Slide 5: Scenarios and assumptions
CRS scenarios
  2 and 4 CRS APs
  Non-colliding CRS dominant interferer and Colliding CRS 2nd dominant interferer (Cell ID pattern (S, I1, I2) = (0,1,6))
Interference models
  PDSCH: Reuse Rel-13/14 CRS-IM interference model with per-TTI interference presence modelling. Further evaluate performance for the case of 0%, 10%, and 20% RU.
  MPDCCH: Same model as for PDSCH.
  PDCCH: Reuse Rel-13 CCIM interference model and power profiles.
Companies are encouraged to provide link level results with analysis of 1RX CRS-IM performance benefits for the identified scenarios in RAN4 #84bis meeting

## Slide 6: Reference receivers
Reference 1RX CRS-IM receiver assumptions
  Single dominant interference cancellation
  Assume CRS assistance is available for studies / requirements definition. Further discuss blind detection of CRS parameters.

## Slide 7: Impact on complexity and power consumption
Confirm that 1RX CRS-IM has acceptable impact on UE implementation complexity and UE power consumption