## Slide 1: Way forward for CRS-IM related advanced receiver impact analysis for network-based CRS-IM
Ericsson
3GPP TSG-RAN WG4 Meeting #84 Berlin, Germany, 21 - 25 August 2017
R4-1708732

## Slide 2: Evaluation plan
CRS-IM PDSCH receivers:
  Assume that eNB always provides UE CRS Assistance information disregards whether CRS muting is used in the neighboring cells
  Further evaluate performance for the cases when neighboring cell has 0% PDSCH loading and for cases w/wo CRS muting.
  The simulation assumptions are captured in next page.
Further investigate impact on Dl Control Channel IM Type A/B and NAICS receivers

## Slide 3: Simulation assumption CRS-IM (for information)
Parameters | value
Bandwidth | 10 MHz
Transmission mode | 3, 9
Number of aggressor cells | 2
Interference level () | 10.45 dB for aggressor cell 1 and 4.6 dB for aggressor cell 2
CRS-IC receiver assumption | Assume full CRS is allocated in the aggressor cells
MCS | 8 and 24
MIMO rank | MIMO rank 1, 2
Resource allocation in serving cell | PRBs 0~9 (Partial resource allocation) PRBs 22~27 (center 6 PRBs) PRBs 0~49 (Full resource allocation)
MIMO configuration | 2x2 (2 CRS APs) Interested companies are welcomed to provide simulation results for 4x2 (4 CRS APs)
Interference modelling | When the CRS is muted, CRS is muted except the center 6 PRBs. When the CRS is not muted, CRS is transmitted across the whole bandwidth. 0% load on interference PDSCH
CRS configuration | Non-colliding CRS is configured
Parameters | value
Bandwidth | 10 MHz
Transmission mode | 3, 9
Number of aggressor cells | 2
 | 10.45 dB for aggressor cell 1 and 4.6 dB for aggressor cell 2
CRS-IC receiver assumption | Assume full CRS is allocated in the aggressor cells
MCS | 8 and 24
MIMO rank | MIMO rank 1, 2
Resource allocation in serving cell | PRBs 0~9 (Partial resource allocation) PRBs 22~27 (center 6 PRBs) PRBs 0~49 (Full resource allocation)
MIMO configuration | 2x2 (2 CRS APs) Interested companies are welcomed to provide simulation results for 4x2 (4 CRS APs)
Interference modelling | When the CRS is muted, CRS is muted except the center 6 PRBs. When the CRS is not muted, CRS is transmitted across the whole bandwidth. 0% load on interference PDSCH
CRS configuration | Non-colliding CRS is configured