## Slide 1: WF on terminology for channel bandwidth
R4-1708846
Ericsson

## Slide 2: Background
Currently in 36.104 the term “channel bandwidth” is defined as:
Channel bandwidth: RF bandwidth supporting a single E-UTRA RF carrier with the transmission bandwidth configured in the uplink or downlink of a cell.
  NOTE: The channel bandwidth is measured in MHz and is used as a reference for transmitter and receiver RF requirements
In 36.101, the definition is:
Channel bandwidth: The RF bandwidth supporting a single E-UTRA RF carrier with the transmission bandwidth configured in the uplink or downlink of a cell. The channel bandwidth is measured in MHz and is used as a reference for transmitter and receiver RF requirements.
The channel bandwidth is always the same between UE and BS, and the definitions are the same

## Slide 3: Background
For NR, it is already agreed that BS and UE may operate different channel bandwidths. Furthermore, the set of “channel bandwidths” for the BS may differ to the UE

## Slide 4: Background
Use of the term “channel bandwidth” will cause confusion in the discussion and specifications on whether UE or BS channel bandwidths are referred to
Also, in the definition, channel bandwidth is referred to as a transmission on a single carrier. The same portion of spectrum may be understood as one carrier for the BS but several carriers for the UE

## Slide 5: Agreement
Separate terms for “UE channel bandwidth” and “BS channel bandwidth”
The definition of UE channel bandwidth and BS channel bandwidth may remain as today or be revised. Proposals for definitions should be made in RAN4 AH#3