## Slide 1: WF on BS ACLR for NR sub6GHz
NTT DOCOMO, INC., Huawei
R4-1708855
3GPP TSG-RAN WG4 Meeting #84
Berlin, Germany, 21-25 August 2017
Agenda Item: 9.3.5.1

## Slide 2: Background
Sub6 ACLR is discussed in [1-3].
This contribution summarizes way forward/agreement on this topic.
[1] R4-1707562 Measurement Bandwidth and required patterns for BS ACLR NTT DOCOMO
[2] R4-1707150 Proposals on below 6GHz NR BS ACLR and ACS Nokia
[3] R4-1707960 Discussion on ACLR and ACS requirement for below 6GHz NR BS ZTE

## Slide 3: Agreements(Measurement BW)
Transmission BW configuration of wanted channel (it would differ depend on SCS, CBW or Band) is used as a measurement BW for wanted signal power measurement (regardless of adjacent RAT).
As below table, for ACLR vs. UTRA/E-UTRA, the same measurement BW is used for adjacent channel power measurement with existing E-UTRA spec. Not to specify vs. other E-UTRA CBW than 5MHz.
No need to specify ACLR vs. UTRA in core spec since it is already covered by ACLR vs. E-UTRA case.
 | Assumed adjacent channel carrier (informative) | Filter on the adjacent channel frequency and corresponding filter bandwidth | ACLR limit
ACLR1 vs E-UTRA | 5MHz E-UTRA | Square (BWConfig of 5MHz E-UTRA) | 45 dB
ACLR2 vs. E-UTRA | 5MHz E-UTRA | Square (BWConfig of 5MHz E-UTRA) | 45 dB
ACLR1 vs. UTRA | 3.84 Mcps UTRA | RRC (3.84 Mcps) | 45 dB
ACLR2 vs. UTRA | 3.84 Mcps UTRA | RRC (3.84 Mcps) | 45 dB

## Slide 4: Agreements(Measurement BW)
For ACLR vs. NR, following options can be considered as a measurement BW for adjacent channel power measurement.
  Option 1: max transmission BW configuration of the CBW (between SCS)
  Option 2: transmission BW configuration of wanted signal (with the same SCS)
    Investigate whether co-existence is guaranteed or not with adjacent channel which uses smaller SCS than own one.
Example) 50MHz CBW for sub6GHz (the value of NRB is a just example)
SCS | NRB | X = BWconfig / BWchannel [%] | Transmission BW config.
15kHz | 270 | 97.2 | 48.6 MHz
30kHz | 133 | 95.8 | 47.88 MHz
60kHz | 65 | 93.6 | 46.8 MHz
 | Measurement BW
Option 1 | 48.6MHz
Option 2 | 48.6 or 47.88 or 46.8 MHz (depend on the SCS of wanted signal)