## Slide 1: WF on NR BS ACS for sub 6GHz
ZTE,Nokia,Ericsson
3GPP TSG-RAN WG4 Meeting #84
Berlin, Germany, 21 - 25 Aug, 2017
Agenda Item: 9.3.5.1
R4-1708856

## Slide 2: Background
Contributions on sub 6GHz ACS have been discussed in RAN4#84:
R4-1707150 Proposals on below 6GHz NR BS ACLR and ACS, Nokia;
R4-1707960 Discussion on ACLR and ACS requirement for below 6GHz NR BS,ZTE;
R4-1708139 NR BS ACS requirementsfor sub-6GHz, Huawei;
R4-1707286 ACLR and ACS for Frequency Ranges <6GHz, AT&T GNS Belgium SPRL;

## Slide 3: Way forward
The following consideration for ACS requirement needs to be taken into account:
Additional frequency offset similar to LTE to avoid orthogonality between sub-carriers of wanted and interfering signal should be considered;
ACS interfering signal should not extend to frequency range of OOB blocking;
Note: frequency offset of OOB blocking to channel edge is still under discussion;
3) Regarding the bandwidth of interfering signal:
Option1 :
Using the same channel bandwidth, the same number of resource blocks and SCS for wanted signal and adjacent interfering signal ;
Option2:
For NR bands less than 100 MHz, it is proposed to specify [5] MHz as the interfering carrier bandwidth for ACS requirements.
For NR bands wider than or equal to 100 MHz, it is proposed to specify [20] MHz as the interfering carrier bandwidth for ACS requirements.