## Slide 1: Way forward on co-location
Agenda Item: 8.28.3.1
Document for: Approval
Source: Nokia, Nokia Shanghai Bell, …
3GPP TSG-RAN WG4 #84 R4-1708890
Berlin, Germany, 21st - 20th April 2017

## Slide 2: Background
During the AAS ad hoc meeting, several co-location requirement contributions [1]-[4] were discussed and some open issues
This way forward is to capture the agreements from this meeting on the open issues:
  Reference antenna definition
  Detailed co-location scenario including a diagram
  d (edge-to-edge co-location distance)

## Slide 3: More detailed figure (for TR37.843)
x
x
d
x = boresight
d = edge to edge distance
h = vertical radiating dimension
Reference antenna
AAS BS
Enclosure
Total area of radiating elements
h
Co-location scenario
h is not specified as an OTA core requirement.

## Slide 4: Agreement (1/2)
d = [10 cm]

## Slide 5: Agreement (2/2)
Definition
  Co-location reference antenna: A single column passive antenna which has the same vertical radiating dimension (h), frequency range, polarization, and coverage area as the composite antenna of AAS at a distance (d) from the edge of the AAS BS.
    Note 1: h and d are described in the figure below
    Note 2: The co-location reference antenna and the AAS do not have to be the same width.
    Note 3. The vertical radiating regions of the co-location reference antenna and the AAS composite antenna are aligned
x
x
d
Reference antenna
AAS BS
h
X denotes direction of boresight (i.e. out of page)

## Slide 6: References
[1] R4-1707565, Discussion for determining the value of “d” for co-location, NTT DOCOMO, INC
[2] R4-1708098, Co-location concept considerations, Ericsson
[3] R4-1708399, Discussion on co-location requirements open issues, Huawei
[4] R4-1708501, eAAS co-location requirements, Nokia, Nokia Shanghai Bell
[5]