## Slide 1: WF on the OTA RX requirements
CMCC
R4-1708956
Agenda :8.28.3.5
Document for: Approval
3GPP TSG RAN WG4 Meeting #84
Berlin, Germany, 21 - 25 August, 2017

## Slide 2
Keep the already agreed OTA RX requirement based on the OTA reference sensitivity.
Add additional IBB, ACS ,IMD OTA test based on minimum sensitivity:
OTA Wanted signal level= minimum sensitivity + 6dB ;
OTA Interference signal level= minimum sensitivity + ∆;
∆ for OTA ACS test =Conducted ACS interference level – P reference;
∆ for OTA IBB test =Conducted blocking interference level – P reference;
∆ for OTA IMD test =Conducted IMD interference level – P reference;
P reference: conducted sensitivity level
Definition of the minimum sensitivity:
Minimum sensitivity is the lowest sensitivity in all declared OSDD.
Minimum sensitivity captures the whole system performance which should includes array gain, baseband combing ability and receiver units ability.
Test direction:
This OTA test is performed in the OSDD which has the minimum sensitivity.
Option1. Use the extreme directions associated with the RoAoA when the receiver target direction is at the reference direction (requires some additional conformance directions declarations).
Option2. Use the existing extreme steering directions at the extremes of the redirection range(declared OSDD)and the reference direction .
Agreement

## Slide 3
[1] R4-1707839, Discussion on eAAS Receiver OTA Requirements, CMCC
[2] R4-1708116, On receiver requirements, Ericsson
[3] R4-1708499, Revisiting OTA reference sensitivity and OTA sensitivity, Nokia, Nokia Shanghai Bell
Reference